## Slide 1: Trinity River Science Symposium Weaverville, CA May 1, 2024
Water temperatures in the Klamath-Trinity Basin:
flow, other key drivers, and
climate change implications
Eli Asarian
Riverbend Sciences

## Slide 2
Understanding thermal regimes
Better management decisions
Improve restoration outcomes

## Slide 3
Outline
Stream temperature background
Klamath Basin studies
Trinity River
Eli Asarian

## Slide 4
Part 1:
Stream temperature background
Eli Asarian

## Slide 5
Energy fluxes:
1) Stream-atmosphere
2) Stream-bed
Advective fluxes:
1) Water movement
Leach et al. 2023

## Slide 6
Watershed area
Relative flux magnitude
Small
Medium
Large
Leach et al. 2023

## Slide 7
Watershed area
Relative flux magnitude
GW & tribs
Small
Medium
Large
Leach et al. 2023

## Slide 8
Watershed area
Relative flux magnitude
Solar radiation
Small
Medium
Large
GW & tribs
Leach et al. 2023

## Slide 9
Jon Grunbaum
Klamath National Forest
Jacob Kann
Aquatic Ecosystem Sciences
Kate Perkins
Environmental Research
Kyle De Juilio & Dave Gaeuman
Yurok Tribe
Todd Buxton
US Bureau of Reclamation
Crystal Robinson
California Dept. of Fish and Wildlife
Lyra Cressey
Salmon River Restoration Council
Aaron David
King County,
Water & Land Resources Division
Frank Lake
USFS PSW Research Station
Eli Asarian
Riverbend Sciences
LeRoy Cyr
Six River National Forest
Toz Soto
Karuk Tribe Dept. of
Natural Resources
Seth Naman
NOAA Fisheries
Part 2 Klamath Basin studies
Photo: Samantha Chilcote

## Slide 10
Photo:James Mitchell
Photo: Michael Hentz
www.westcoast.fisheries.noaa.gov
Spring-run Chinook Salmon
Oncorhynchus tshawytscha
NMFS PRD
Steelhead trout
Oncorhynchus mykiss
Dams
Derek Acomb, CDFW
Coho salmon
Oncorhynchus kisutch
Salmon R

## Slide 11
Stream Temperature Data Sources
Logos for illustration only, does not imply endorsement
Notes: Projects compile data from nearly all available sources.

## Slide 12
Photo: Michael Hentz
Photo: Michael Hentz
Dams
Trinity
Salmon
Scott
Shasta
SF Trinity
Mainstem
Trinity
Salmon
Lower Klamath
SF Trinity
Mid/Lower Klamath
Flow
Scott & others
Wildfire smoke
Upper Klamath

## Slide 13
  Water temperature responses to climate
  vary according to site characteristics and day of year
Eli Asarian
Eli Asarian
SRRC

## Slide 14
Mid/Lower Klamath
Salmon R.
Scott R.
Shasta R.
Middle Klamath R.
Lower Klamath R.
  85 sites ≥14 years data
  1995–2017
Asarian et al. 2020
Iron Gate
Dam
JC Boyle Dam

## Slide 15
Legend:
Warming
Cooling
Effect of Climate Predictors on Stream Temperature
Coefficient estimate and 95% confidence interval (standardized units)
Asarian et al. 2020

## Slide 16
Legend:
Warming
Cooling
Effect of Climate Predictors on Stream Temperature
Coefficient estimate and 95% confidence interval (standardized units)
Asarian et al. 2020

## Slide 17
Legend:
Warming
Cooling
Effect of Climate Predictors on Stream Temperature
Coefficient estimate and 95% confidence interval (standardized units)
Asarian et al. 2020

## Slide 18
Legend:
Warming
Cooling
Effect of Climate Predictors on Stream Temperature
Coefficient estimate and 95% confidence interval (standardized units)
Asarian et al. 2020

## Slide 19
Stream Temp. Long-Term Trends 1995-2017 (All Sites Combined)
Increasing
Decreasing
Annual
maximum
Annual maximum
Asarian et al. 2020

## Slide 20
Stream Temp. Long-Term Trends 1995-2017 (All Sites Combined)
July is increasing fastest
Increasing
Decreasing
Annual
maximum
Annual maximum
Asarian et al. 2020

## Slide 21
Increasing
Decreasing
Cooling effect of flow (Flow random slope)
Strong effect
weak effect
Asarian et al. 2020

## Slide 22
Increasing
Decreasing
Cooling effect of flow (Flow random slope)
Strong effect
Salmon River Spring-run Chinook salmon habitat
weak effect
Asarian et al. 2020
www.westcoast.fisheries.noaa.gov
Spring-run Chinook Salmon
Oncorhynchus tshawytscha

## Slide 23
South Fork Salmon R. upstream of Black Bear Creek
Little North Fork Salmon R
Asarian et al. 2020

## Slide 24
Little North Fork Salmon R:
South Fork Salmon R. upstream of Black Bear Creek:
Highly sensitive to flow
Trend: steep increase
Asarian et al. 2020

## Slide 25
South Fork Salmon R. upstream of Black Bear Creek:
Highly sensitive to flow
Trend: steep increase
Little North Fork Salmon R:
Less sensitive to flow
Trend: increasing slower
Asarian et al. 2020

## Slide 26
Smoke
May
Jun
Jul
Aug
Sep
South Fork Salmon R. upstream of Black Bear Creek:
Highly sensitive to flow
Trend: steep increase
Little North Fork Salmon R:
Less sensitive to flow
Trend: increasing slower
Asarian et al. 2020

## Slide 27
Smoke
May
Jun
Jul
Aug
Sep
South Fork Salmon R. upstream of Black Bear Creek:
Highly sensitive to flow
Trend: steep increase
Little North Fork Salmon R:
Less sensitive to flow
Trend: increasing slower
Asarian et al. 2020

## Slide 28
Wildfire smoke
Photo credit:
Jonathon McNally (Instagram: @jmc280 & @mountainbladerunner)
David et al. 2018, SRRC 2021
Notes: Less solar radiation also means cooler air temps which also contributes to cooling the water.

## Slide 29
Wildfire smoke reflects solar radiation
Less
radiation
to water
Cooler air temperature
Cooler water
Less stressful for fish
Photo credit:
Jonathon McNally (Instagram: @jmc280 & @mountainbladerunner)
David et al. 2018, SRRC 2021
Notes: Less solar radiation also means cooler air temps which also contributes to cooling the water.

## Slide 30
Smoke cooling greatest in
rivers and large streams
Asarian et al. 2020
Photo credit:
Mid-Klamath Watershed Council
Photo credit:
Eli Asarian
10 km2
0.1 °C cooling
(e.g., Aikens Cr.)
1,946 km2
2.4 °C cooling
(e.g., Salmon River)
270 km2
1.5 °C cooling
(e.g., Beaver Cr.)
Photo credit:
Google Street View

## Slide 31
When and where does
flow affect temperatures?

## Slide 32
Daily temperature model
Generalized additive model (GAM)
Water temp = day + air temp + flow + flow:day + autocorrelation
Average error 1 °C
Asarian et al. 2023 WRR

## Slide 33
Daily flow scenarios at example site (Scott River)
Asarian et al. 2023 WRR
Flow scenario inputs
Highest flow
(0.9 quantile)
Lowest flow
(0.1 quantile)

## Slide 34
Daily flow scenarios at example site (Scott River)
Flow scenario inputs
Modeled stream temperature
Highest flow
(0.9 quantile)
Lowest flow
(0.1 quantile)
Highest
flow
(0.9 quantile)
Lowest flow
(0.1 quantile)
Difference
(Lowest flow minus Highest flow)
Asarian et al. 2023 WRR

## Slide 35
Modeled temperature difference (°C) between lowest & highest flow
scenarios
Asarian et al. 2023 WRR

## Slide 36
Asarian et al. 2023 WRR
Warming
Cooling
Isaak et al. 2018

## Slide 37
Asarian et al. 2023 WRR
Isaak et al. 2018
Warming
Cooling
Warming
Cooling
FitzGerald et al. 2021

## Slide 38
Future 2070–2099 High Emissions (RCP8.5)
Mean Daily Max. August Temp. (°C)
Baseline 1990–2017
N.F Salmon R.
Wooley Cr.
S.F.
Salmon R.
Mainstem
Salmon R.
Little N.F.
Salmon R.
N.F Salmon R.
Wooley Cr.
S.F.
Salmon R.
Mainstem
Salmon R.
Little N.F.
Salmon R.
Asarian et al. 2019 Salmon

## Slide 39
Baseline vs
2070-2099 High Emissions (RCP8.5)
SF Salmon is
Most sensitive
N.F Salmon R.
Wooley Cr.
S.F.
Salmon R.
Mainstem
Salmon R.
Little N.F.
Salmon R.
Mean Daily Max. August Temp. Increase (°C)
Asarian et al. 2019 Salmon

## Slide 40
Baseline vs
2070-2099 High Emissions (RCP8.5)
SF Salmon is
Most sensitive
N.F Salmon R.
Wooley Cr.
S.F.
Salmon R.
Mainstem
Salmon R.
Little N.F.
Salmon R.
Mean Daily Max. August Temp. Increase (°C)
Asarian et al. 2019 Salmon
Scenario | Stream temperature increase from baseline
High Emissions (RCP 8.5) | 1.7–3.2 °C
Moderate emissions (RCP 4.5) | 0.9–2.0 °C

## Slide 41: Part 2 Conclusions
Photo: Salmon River Restoration Council
Responses to climate vary according to site characteristics and day of year

## Slide 42: Part 2 Conclusions
Drivers
  effect greatest in rivers and large streams
  effect greatest in April-July
Trends
  Greatest increases in July
  limiting rises in August stream temps
  Site-specific responses vary
    Rising air temperature
    Flow-sensitive tribs warming faster
Photo: Salmon River Restoration Council
Responses to climate vary according to site characteristics and day of year

## Slide 43
Cold water contracts upstream
  Need passage
Photo: Eli Asarian
Tributary refugia increasingly important
  Need to protect/increase cold water
Part 2 Conclusions

## Slide 44
Photo: Michael Hentz
Photo: Michael Hentz
Mainstem
Trinity
Salmon
Lower Klamath
SF Trinity
Mid/Lower Klamath
Flow
Scott & others
Wildfire smoke
Upper Klamath
https://www.riverbendsci.com/reports-and-publications

## Slide 45
Part 3:
Trinity River
Temperature Synthesis Report

## Slide 46
Objectives
Compile comprehensive quality-controlled water temperature dataset
Evaluate:
  Relationship between flow and temperature in time and space
  Temperature effects on biological objectives
  Temperature compliance with regulatory objectives
Update conceptual models
Develop management recommendations
Photo: USBR

## Slide 48
Deep cold releases,
No surface release
Regulates flow
Thermally stratified
Cold pool depleted in severe droughts

## Slide 49
Regulates flow
Thermally stratified
Cold pool depleted in severe droughts
Deep cold releases,
No surface release
Warming depends on residence time, decreased since 1990s

## Slide 50
Lewiston
to Douglas City
450 cfs cold baseflow for spring chinook,
replacing inaccessible habitat above dam

## Slide 51
Lewiston
to Douglas City
450 cfs cold baseflow for spring chinook,
replacing inaccessible habitat above dam
Temperatures highly affected by dam release quantity
Douglas City
to North Fork
ROD spring high flow releases:
temps too cold (<13 °C) for optimal juvenile chinook growth
until after most juveniles have already migrated downstream

## Slide 52
Lewiston
to Douglas City
450 cfs cold baseflow for spring chinook,
replacing inaccessible habitat above dam
Temperatures highly affected by dam release quantity
Douglas City
to North Fork
ROD spring high flow releases:
temps too cold (<13 °C) for optimal juvenile chinook growth
until after most juveniles have already migrated downstream
Lower Trinity R.
Dam release effects vary with season, trib temps, and flows
ROD releases May–July to maintain cool temps for smolts. Up to 3 °C cooler than pre-dam
<1 °C cooling during summer baseflow

## Slide 53
Lewiston
to Douglas City
450 cfs cold baseflow for spring chinook,
replacing inaccessible habitat above dam
Temperatures highly affected by dam release quantity
Douglas City
to North Fork
ROD spring high flow releases:
temps too cold (<13 °C) for optimal juvenile chinook growth
until after most juveniles have already migrated downstream
Lower Trinity R.
Dam release effects vary with season, trib temps, and flows
ROD releases May–July to maintain cool temps for smolts. Up to 3 °C cooler than pre-dam
<1 °C cooling during summer baseflow
Klamath temps similar to Trinity except during unnaturally high flow releases from Trinity Reservoir

## Slide 54
Controls spring runoff
Climate change:
snow to rain, earlier runoff
Unregulated tribs
including upstream of dam
Temps of largest tribs similar to pre-dam river
Temps warm as flow declines in spring,
hot in mid-summer
Mountain snowpack

## Slide 55
Controls spring runoff
Climate change:
snow to rain, earlier runoff
Small tributaries to Lower Trinity R. provide summer/fall thermal refugia
Unregulated tribs
including upstream of dam
Temps of largest tribs similar to pre-dam river
Temps warm as flow declines in spring,
hot in mid-summer
Most tributaries
to Upper Trinity R. are
warmer than river in late spring and summer
Mountain snowpack

## Slide 56
Channel rehabilitation
to restore
thermally-diverse
off-channel &
edge habitats

## Slide 57: Modeling Unimpaired (no-dam) Temperatures at Lewiston
Daily timestep
Generalized additive model (GAM)
Predictors:
Day, Air temp, Flow, Flow:day, autocorrelation
Calibration: 1942–1946 & 1958–1961
Notes: Figure 22. Comparison of measured and leave-one-year-out cross-validated predictions for daily mean water temperatures in the Trinity River at Lewiston for 1942–1946 and 1958–1961, prior to dam regulation. Model uses air temperature, flow, day of year, and autocorrelation. Data sources for observed water temperature: Moffett and Smith (1950), Murray (1960, 1961), and USGS (gage 11525500).
RMSE = root mean squared error (a measure of prediction accuracy), R2 = coefficient of determination ranging from 1 (perfect correlation) to 0 (complete lack of relationship between the variables), and n = number of days with measured temperature data. Solid black line is linear regression prediction and dashed line is 1:1 line.
Figure 23. Daily time series of air temperature, water temperature, and flow for the Trinity River at Lewiston for 1942–1946 and 1958–1961, prior to dam regulation. Data sources: air temperature from gridded models (Livneh et al. 2013, Daly et al. 2008); measured water temperature from Moffett and Smith (1950), Murray (1960, 1961), and USGS (gage 11525500); modeled water temperature data from our analysis; and flow from USGS (gage 11525500).
Dashed lines represent typical conditions, calculated as period-of-record (air temperature: 1915–2019, flow: 1911–1961 measured and 1963–2019 estimated unimpaired) median for each day of the year, smoothed with a 7-day average for legibility. Due to the short period of record, a typical conditions dashed line is not shown for water temperature.

## Slide 58: Modeling Unimpaired (no-dam) Temperatures at Lewiston
Daily timestep
Generalized additive model (GAM)
Predictors:
Day, Air temp, Flow, Flow:day, autocorrelation
Calibration: 1942–1946 & 1958–1961
Generated unimpaired flow and temperature record for 1963–2019
  - New boundary condition for RBM10 scenarios
Notes: Figure 22. Comparison of measured and leave-one-year-out cross-validated predictions for daily mean water temperatures in the Trinity River at Lewiston for 1942–1946 and 1958–1961, prior to dam regulation. Model uses air temperature, flow, day of year, and autocorrelation. Data sources for observed water temperature: Moffett and Smith (1950), Murray (1960, 1961), and USGS (gage 11525500).
RMSE = root mean squared error (a measure of prediction accuracy), R2 = coefficient of determination ranging from 1 (perfect correlation) to 0 (complete lack of relationship between the variables), and n = number of days with measured temperature data. Solid black line is linear regression prediction and dashed line is 1:1 line.
Figure 23. Daily time series of air temperature, water temperature, and flow for the Trinity River at Lewiston for 1942–1946 and 1958–1961, prior to dam regulation. Data sources: air temperature from gridded models (Livneh et al. 2013, Daly et al. 2008); measured water temperature from Moffett and Smith (1950), Murray (1960, 1961), and USGS (gage 11525500); modeled water temperature data from our analysis; and flow from USGS (gage 11525500).
Dashed lines represent typical conditions, calculated as period-of-record (air temperature: 1915–2019, flow: 1911–1961 measured and 1963–2019 estimated unimpaired) median for each day of the year, smoothed with a 7-day average for legibility. Due to the short period of record, a typical conditions dashed line is not shown for water temperature.

## Slide 59
Trinity R at Lewiston
Before dams
  - Thermal maxima in Jul/Aug
With dams:
  - Warmer in the winter
  - Colder in the summer
Notes: Figure 27. Daily mean water temperature time series for Trinity River at Lewiston 1963–2019, colored by water year type, showing (A) temperatures in a modeled no-dams unimpaired flow scenario, (B) measured with-dam temperatures, and (C) difference between the two.
Thin lines are individual years while thick lines are LOESS (LOcally Estimated Scatterplot Smoothing) smoothers.

## Slide 60
1911–1961
Pre-dam era
1963–1978
With-dam full diversion era
1978–1999
With-dam transitional era
2000–2019
With-dam ROD era
1963–2019
Unimpaired flow scenario
Water temp. daily mean (°C)
Flow (cfs) log scale
Trinity R at Lewiston: Flow and Temp by Era
Summer baseflow:
150 cfs
Summer baseflow
300 cfs 1978
450 cfs 1993

## Slide 61
Flows and Diversion
Shift to spring and summer
Notes: Figure 18. Comparison of monthly flow timing in the Trinity River at Lewiston (USGS gage 11525500) and the Carr Diversion (USGS gage 11525430) for three eras: pre-dam (1911– 1/20/1961), with-dam full diversion (10/31/1963–4/30/1978), with-dam transitional (5/1/1978–9/30/1999), and with-dam ROD (10/1/1999–2019). The sum of these two sites (i.e., total height of the stacked bars) is the total outflow of Lewiston Reservoir.
Values were derived by calculating total flows within each time period and month at the two sites, and then dividing by the total flow (summing all months at both sites) within the time period. Partial hydrologic years (i.e., 1961, 1964, and 1978) were excluded from this graph.

## Slide 62
ROD flows “kink” spring warming pattern
Water temperature (°C)
Notes: Figure 41. Daily minimum, mean, and maximum water temperatures measured in the Trinity River at Lewiston for 1942–2019, comparing the pre-dam era (1942–1/20/1961), with-dam full diversion era (10/31/1963–4/30/1978), with-dam transitional era (5/1/1978–9/30/1999), and with-dam ROD era (10/1/1999–2019).
Symbols (circles and triangles) are monthly means with April–July labeled, thin lines are daily time series, and thick lines are LOESS (LOcally Estimated Scatterplot Smoothing) smoothers. USGS Burnt Ranch temperatures for 1961–1983 are extremely variable from year to year, suggesting they may be unreliable. The 1/21/1961–10/30/1963 initial dam-filling period is not shown.

## Slide 63
No “kink” at Hoopa or Weitchpec
“kink” at Burnt Ranch
Water temperature (°C)
Notes: Figure 41. Daily minimum, mean, and maximum water temperatures measured in the Trinity River at Lewiston for 1942–2019, comparing the pre-dam era (1942–1/20/1961), with-dam full diversion era (10/31/1963–4/30/1978), with-dam transitional era (5/1/1978–9/30/1999), and with-dam ROD era (10/1/1999–2019).
Symbols (circles and triangles) are monthly means with April–July labeled, thin lines are daily time series, and thick lines are LOESS (LOcally Estimated Scatterplot Smoothing) smoothers. USGS Burnt Ranch temperatures for 1961–1983 are extremely variable from year to year, suggesting they may be unreliable. The 1/21/1961–10/30/1963 initial dam-filling period is not shown.

## Slide 64
7DADA water temp. (°C)
Shading is 13-16.5 °C juvenile growth target
Juvenile Salmonid Growth
Roger Tabor USFWS
Notes: Figure 60. Measured and modeled 7-day average daily average (7DADA) water temperatures and proposed juvenile salmonid growth targets (dashed horizontal lines at 13–16.5 °C) in the Trinity River Above North Fork where the target is proposed for April-July, arranged by actual water year type and era. Douglas City and Weitchpec are shown for comparison.
Some measured temperatures are estimated by regression with adjacent stations (Section B.7 in Appendix B). For modeled unimpaired scenario, only days with Lewiston flows >350 cfs are included.

## Slide 65
ROD flows:
reduced duration of optimal growth
Juvenile Salmonid Growth
% of June days in Normal, Wet, and Ex Wet years with optimal temps:
47% 1978-1999
9% 2000-2019
7DADA water temp. (°C)
Roger Tabor USFWS
Notes: Figure 60. Measured and modeled 7-day average daily average (7DADA) water temperatures and proposed juvenile salmonid growth targets (dashed horizontal lines at 13–16.5 °C) in the Trinity River Above North Fork where the target is proposed for April-July, arranged by actual water year type and era. Douglas City and Weitchpec are shown for comparison.
Some measured temperatures are estimated by regression with adjacent stations (Section B.7 in Appendix B). For modeled unimpaired scenario, only days with Lewiston flows >350 cfs are included.

## Slide 66
Biological modeling
Modeled no-dam unimpaired flow scenario as baseline
RBM10: temperature
Spreadsheet models: growth and development
Foothill
yellow-legged frog
metamorphosis
Time (days)
Chironomidae midge generation time (days)
Baetidae mayfly generation time
(days)
Temperature
(°C)
Salmonid growth rate (%)
No-dam unimpaired flow scenario
Macroinvertebrates.org
Macroinvertebrates.org
Roger Tabor USFWS
Notes: Figure 62. Display of seasonal trend, from February-June, for five metrics for the unimpaired scenario used to evaluate longitudinal and seasonal dimensions of the thermal landscape of the Trinity River, for FYLF metamorphosis time (p), Chironomidae generation time (c), Baetidae generation time (b), Temperature (U), and salmonid growth (f).

## Slide 67
Biological modeling
Colder temperatures
Reduce salmonid growth rate
Increase invertebrate generation time
Increase frog metamorphisis time
Modeled no-dam unimpaired flow scenario as baseline
RBM10: temperature
Spreadsheet models: growth and development
Foothill
yellow-legged frog
metamorphosis
Time (days)
Chironomidae midge generation time (days)
Baetidae mayfly generation time
(days)
Temperature
(°C)
Salmonid growth rate (%)
No-dam unimpaired flow scenario
Macroinvertebrates.org
Macroinvertebrates.org
Roger Tabor USFWS
Notes: Figure 62. Display of seasonal trend, from February-June, for five metrics for the unimpaired scenario used to evaluate longitudinal and seasonal dimensions of the thermal landscape of the Trinity River, for FYLF metamorphosis time (p), Chironomidae generation time (c), Baetidae generation time (b), Temperature (U), and salmonid growth (f).

## Slide 68
Flow effects on temperature and juvenile salmonid growth rate
(example: Normal water year type)
Flow scenario
Temperature
difference from unimpaired (°C)
Salmonid growth
difference from unimpaired (%/day)
Roger Tabor USFWS
Notes: Figure 60. Measured and modeled 7-day average daily average (7DADA) water temperatures and proposed juvenile salmonid growth targets (dashed horizontal lines at 13–16.5 °C) in the Trinity River Above North Fork where the target is proposed for April-July, arranged by actual water year type and era. Douglas City and Weitchpec are shown for comparison.
Some measured temperatures are estimated by regression with adjacent stations (Section B.7 in Appendix B). For modeled unimpaired scenario, only days with Lewiston flows >350 cfs are included.

## Slide 69
Time difference relative to unimpaired
Faster
Slower
Flow scenario
Flow effects on development time
(example: Normal water year type)
Foothill yellow-legged frog
metamorphosis time
Chironomidae midge generation time
Baetidae mayfly generation time
Macroinvertebrates.org
Macroinvertebrates.org
Notes: Figure 60. Measured and modeled 7-day average daily average (7DADA) water temperatures and proposed juvenile salmonid growth targets (dashed horizontal lines at 13–16.5 °C) in the Trinity River Above North Fork where the target is proposed for April-July, arranged by actual water year type and era. Douglas City and Weitchpec are shown for comparison.
Some measured temperatures are estimated by regression with adjacent stations (Section B.7 in Appendix B). For modeled unimpaired scenario, only days with Lewiston flows >350 cfs are included.

## Slide 70
Steel et al. 2017
Lateral thermal diversity
Notes: Steel, E.A., T.J. Beechie, C.E. Torgersen, and A.H. Fullerton, 2017. Envisioning, Quantifying, and Managing Thermal Regimes on River Networks. BioScience 67:506–522. doi: 10.1093/biosci/bix047.

## Slide 71
Steel et al. 2017
Lateral thermal diversity
Notes: Steel, E.A., T.J. Beechie, C.E. Torgersen, and A.H. Fullerton, 2017. Envisioning, Quantifying, and Managing Thermal Regimes on River Networks. BioScience 67:506–522. doi: 10.1093/biosci/bix047.

## Slide 72
Floodplain
Streambed
Notes: Floodplains tend to have shallower depths and lower velocities, allowing the air temperature to act on the water more than in the turbulently mixed stream channel. Similar to the vertical dimension, this allows for a lot of thermal diversity over a relatively small geographic area at the same time. However, unlike in the vertical dimension, this happens during high flows, instead of low flows.

## Slide 73
Notes: Studies in the Sacramento river basin have found that the floodplains have a tremendous amount of food, due to several factors, but one is warmer temperatures.

## Slide 74: Lateral thermal diversity
SRH-2D modeling of Oregon Gulch restoration site (e.g., 7/25/2019, 700 cfs)
Impaired pre-project channel is thermally homogenous
Topographically influenced thermal diversity could be substantial at channel rehab sites
Thermal diversity: New evaluation metric for restoration site designs?
Notes: Figure 71. Map of modeled temperature output for pre-project (left) and design (right) conditions in the Oregon Gulch reach computed with meteorology and hydrology inputs for extremely wet hydrology on July 25th, 2019, and a modeled flow of 700 cfs.
Flow direction is from the bottom of the image to the top. Temperature categories are based on thresholds for juvenile salmonid growth from Carter (2005), where growth ceases at <5 °C, growth reduced by >20% at 5-10 °C, growth reduced by 10–20% at 10–13.5 °C, growth reduced by <10% at 13.5–16 °C, maximum growth range and increased prevalence of disease at 16–20 °C, growth reduced <20% and high prevalence of disease at 20–24.5 °C, and >24.5 °C is unsuitable for salmonids.

## Slide 75
Existing condition – 1200cfs
Design condition – 1200 cfs

## Slide 77
Trinity Reservoir
Photo: USBR
Notes: Figure 15. Reservoir water storage in Trinity Reservoir from November 1960 to September 2019. Data from USGS site 11525400. Dashed line at 0.75 million acre-feet (MAF) indicates the carryover storage level below which may be potentially thermally problematic for cold water fish in the Trinity River (Bender 2012).
Minimum storage less than 0.75 MAF are labeled.

## Slide 78
Trinity Reservoir stratification
Depth (ft)
Warmer surface water is present, but no way to release it
No temperature control device
Notes: Figure 15. Reservoir water storage in Trinity Reservoir from November 1960 to September 2019. Data from USGS site 11525400. Dashed line at 0.75 million acre-feet (MAF) indicates the carryover storage level below which may be potentially thermally problematic for cold water fish in the Trinity River (Bender 2012).
Minimum storage less than 0.75 MAF are labeled.

## Slide 79
Trinity Reservoir storage
Notes: Figure 15. Reservoir water storage in Trinity Reservoir from November 1960 to September 2019. Data from USGS site 11525400. Dashed line at 0.75 million acre-feet (MAF) indicates the carryover storage level below which may be potentially thermally problematic for cold water fish in the Trinity River (Bender 2012).
Minimum storage less than 0.75 MAF are labeled.

## Slide 80
Trinity Reservoir
Notes: Figure 13. Comparison of the 1972–1990 and 1998–2019 time periods for the relationship of Trinity Reservoir storage volume to water temperatures at elevations of main outlet (2114 ft) and auxiliary outlet (2000 ft) for all months (January–December) in 38 years from 1972–2019, excluding years without data. Data extracted from reservoir profiles measured by USBR (2020). At low reservoir storage, a few high temperature values cause the blue trend line for 1973–1990 be higher than red trend line for the 1998–2019, but this an artifact of particular conditions that occurred in 1977 and not representative of the overall period.
Lines are LOESS (LOcally Estimated Scatterplot Smoothing) smoothers. Concept for figure adapted from Barajas (2016).
In the 1973–1990 period, 1977 was the only year for which profiles are available when storage was below 1 million acre-feet. Due to extremely low inflow, in 1977 the reservoir never fully cooled down, so started the year warm and temperatures rose to high levels much earlier than in other years (Figure 12).

## Slide 81
Trinity Reservoir
Coldest water has warmed 1 °C
Temperatures increase during drought drawdowns
Notes: Figure 13. Comparison of the 1972–1990 and 1998–2019 time periods for the relationship of Trinity Reservoir storage volume to water temperatures at elevations of main outlet (2114 ft) and auxiliary outlet (2000 ft) for all months (January–December) in 38 years from 1972–2019, excluding years without data. Data extracted from reservoir profiles measured by USBR (2020). At low reservoir storage, a few high temperature values cause the blue trend line for 1973–1990 be higher than red trend line for the 1998–2019, but this an artifact of particular conditions that occurred in 1977 and not representative of the overall period.
Lines are LOESS (LOcally Estimated Scatterplot Smoothing) smoothers. Concept for figure adapted from Barajas (2016).
In the 1973–1990 period, 1977 was the only year for which profiles are available when storage was below 1 million acre-feet. Due to extremely low inflow, in 1977 the reservoir never fully cooled down, so started the year warm and temperatures rose to high levels much earlier than in other years (Figure 12).

## Slide 82
Trinity Reservoir
Notes: Figure 14. Relationship of Trinity Reservoir storage volume to water temperatures at main outlet elevation (2114 ft) for all months (January–December) in 38 years from 1972–2019, excluding years without data. Data extracted from reservoir profiles measured by USBR (2020). Lines are LOESS (LOcally Estimated Scatterplot Smoothing) smoothers. Vertical dashed line at 1,250 thousand acre-feet (AF) indicates approximate slope break below which temperatures rise steeply as reservoir storage declines, in months when reservoir thermally stratification is stronger (April-November).
Concept for figure adapted from Barajas (2016).

## Slide 83
Salmonid egg survival versus temperature
Beacham and Murray 1990
Coho salmon egg survival rapidly falls at temps >12°C
Florian Graner USFWS

## Slide 84: Trinity River at Lewiston temperatures
Thermal maxima in November

## Slide 85: Measured hatchery Coho Salmon egg survival 2021
Data provided by CDFW
Florian Graner USFWS

## Slide 86
Climate Change: Snowpack
Snowpack >3,000 ft elevation:
  11.6 inches in 1981-2010
  1.6 inches in 2070-2099
Micheli et al. 2018
Notes: Figure 75. Projected monthly average inflow into Trinity Reservoir for 1922–2003 (labeled as 2010), 2025, and 2060 from the California Water Fix/Bay Delta Conservation Plan (CDWR and USBR 2016). taf = thousand acre-feet.
Figure 76. Historical Trinity Reservoir water storage for 1961–2010 compared with three projected scenarios: EBC2 is the 2010 timeframe, EBC2_ELT is the 2025 timeframe, EBC2_LLT is the 2060 timeframe (and the NEPA No Action Alternative). Figure adapted from the California Water Fix/Bay Delta Conservation Plan (CDWR and USBR 2016).

## Slide 87
Rain
Earlier runoff
Snow
Trinity Reservoir climate challenges
Photo: USBR
Mote et al. 2014
Notes: Climate-driven transition from snow to rain is well known.

## Slide 88
Rain
Earlier runoff
Snow
Flood control releases
Water storage
Cold-water pool
Trinity Reservoir climate challenges
Photo: USBR
Notes: But most people underappreciate much this is going to impact reservoir management. For dam safety reasons, reservoirs are going need to maintain large flood control capacity, reducing effective storage. In reservoirs such as Trinity Lake, temperatures of dam releases are highly influenced by how much water is in the reservoir. Low storage during fall could cook salmon eggs and embryos in the river downstream.

## Slide 89
Climate Change: Reservoir Storage
Substantially reduced storage with status quo operation by 2060
CDWR & USBR 2016
Notes: Figure 75. Projected monthly average inflow into Trinity Reservoir for 1922–2003 (labeled as 2010), 2025, and 2060 from the California Water Fix/Bay Delta Conservation Plan (CDWR and USBR 2016). taf = thousand acre-feet.
Figure 76. Historical Trinity Reservoir water storage for 1961–2010 compared with three projected scenarios: EBC2 is the 2010 timeframe, EBC2_ELT is the 2025 timeframe, EBC2_LLT is the 2060 timeframe (and the NEPA No Action Alternative). Figure adapted from the California Water Fix/Bay Delta Conservation Plan (CDWR and USBR 2016).

## Slide 90
Major Findings
ROD era flow releases unnaturally reduced spring temperatures, reducing growth
Flows and temperatures from Lewiston Dam cannot be manipulated separately in an effective manner
Trinity Reservoir:
  Temperatures are warming
  At storage less than 750 TAF, warm release temperatures can threaten spawning adult salmonids
  Storage and warm fall releases will be exacerbated by climate change

## Slide 91
Recommendations
Monitor temperatures upstream of Trinity Reservoir to understand
  Natural temperature regime
  Effects on temperatures in Trinity Reservoir
Until a temperature control device is installed in Trinity Reservoir, for optimal juvenile salmonid growth (13-16.5 °C), flows in spring months should recede beginning in:
  April of Dry and Critically Dry years
  May of Normal and wetter years
Reduce emphasis on meeting ROD temperature targets for smoltification at Weitchpec. Instead, balance:
  Growth
  Encouraging timely outmigration
  Mitigating temperatures in the lower river as they approach the thermal limits of juvenile salmonids.
Photo: USBR

## Slide 92
Modify infrastructure to enable flow and temperature management actions:
  Installation of a multi-level temperature control device in Trinity Reservoir
  Removal of Lewiston Dam, or a new type of conveyance through or around Lewiston
Adhere to end of September storage minimum of 750,000 acre-feet per Bender (2012) recommendations.
Develop multi-year drought contingency plan
  Assess multiyear drought effects on Trinity Reservoir storage levels, water temperatures, and ability to meet temperature criteria
  Specifies steps taken when reservoir storage is predicted to be less than 1,250,000 acre-feet in any year, assuming a multi-year drought is possible at any time
Recommendations continued

## Slide 93
Extra slides
Notes: 2000 was the beginning of TRRP/restoration, and river allocation increased to around 50%

## Slide 94
Methods
Time separated into four eras
  Pre-dam era (1911–1961)
  Full diversion era (1963–1978)
  Transitional era (1978–1999)
  ROD era (2000–2019)*
Datasets gathered from
  USFWS
  USGS
  USFS
  Hoopa Tribe
  Yurok Tribe
  Others
Statistical and modeling
  RBM10
  FYFAM, invertebrate lifecycle, salmonid bioenergetics
  SRH-2D
  Climate change models
  Reservoir dynamics
  Gap filling
  Linear regression, linear mixed effects models, generalized additive models, and LOESS.
Notes: 2000 was the beginning of TRRP/restoration, and river allocation increased to around 50%

## Slide 95
Adult Salmonid Disease Prevention Flows
Notes: Modeled with RBM10

## Slide 96
Ceremonial Release Flows
Notes: Modeled with RBM10

## Slide 97
Cooling of Klamath River from Lewiston releases increase to ~1,450 cfs, then tapers off
RBM10 results are 1.7 °C/1000 cfs of cooling
RBM10 appears to overestimate cooling effect of Trinity on lower Klamath due to underestimating Klamath flows (hopefully fixing soon!)
Summer cooling of Lower Klamath River from Trinity Releases
Notes: Relationship between Lewiston Reservoir releases above 450 cfs summer baseflows and RBM10 estimates of daily average temperature (°C) changes resulting from the additional flow releases. Each point represents a day in Mid-August through late September in 2003–2004, 2012–2016, and 2018 when releases were made from Lewiston Reservoir into the Trinity River intended to improve Lower Klamath River conditions. Temperature changes are computed as the temperature of augmentation release scenario minus temperature of summer baseflow scenario.

## Slide 98
Thank you!
  Reclamation
  USFWS
  USGS
  USFS
  NOAA
  Hoopa Tribe
  Yurok Tribe
  Other collaborators
Report available: https://www.trrp.net/library/document/?id=2615