## Slide 1: Physical objectives on the Trinity River, CA
Topographic variability Inundation effectiveness Active bars Channel migration Fine sediment storage Thresholds for sediment mobility Bed mobility and scour Management actions for all include flow releases, channel rehabilitation, gravel augmentation, and sometimes others.

## Slide 2: Topographic variability
Definition: Topographic variability is the range in channel bed elevations relative to the water surface at a given flow.
Objective: Increase topographic variability.
Justification: Topographic variability is an attribute of a spatially complex channel. A complex channel is more likely to support the lifecycle needs of inhabitants of the river biome than a simplified channel.
Frequency and domain for evaluation: When channel bathymetry is surveyed for a reach of river.

## Slide 3: Inundation effectiveness
Definition: The valley width that is inundated by flow is effective when it provides enough habitat to support a biologically healthy river.
Objective: Increase the average wetted width of flow at a range of discharges.
Justification: Habitat areas for fish and riparian plants are likely to increase with the wetted width of the channel.
Frequency and domain for evaluation: When channel bathymetry is surveyed for a reach of river.

## Slide 4: Active bars
Definition: An active bar is an unvegetated deposit of sediment in the active channel of the river.
Objective: Increase the area of active bars that is exposed at summer baseflow to within ranges targeted for distinct reaches of the Trinity River.
Justification: Active bars promote physical and ecological processes that are endemic to healthy alluvial channels.
Frequency and domain for evaluation: Every five years for the entire restoration reach.

## Slide 5: Channel migration
Definition: Channel migration occurs when the river erodes its banks and changes its position between valley walls.
Objective: Increase the amplitude of river meanders through time.
Justification: River meandering constructs new alluvial features and floodplains and recruits woody material to the channel. Meanders provide a diversity of topographic and hydraulic conditions for the river’s biology.
Frequency and domain for evaluation: Every five years for the entire restoration reach.

## Slide 6: Fine sediment storage
Definition: Fine sediment is particles that are 8 mm or smaller.
Objective: Maintain the calculated hiding function exponent at values greater than -0.9a and ratios of the median surface grain diameter and average subsurface grain diameter both to the median bedload diameter at >1.0b.
Justification: With a), fine sediments are more mobile than coarse grains due to their smaller size and because they are stored in sufficient quantities on the streambed. With b), the target infers fines are sufficiently present for their primary source areas to be subsurface areas of the channel bed and patches in lee areas and near the channel margins.
Frequency and domain for evaluation: When sediment transport monitoring occurs at Douglas City, Limekiln Gulch, and Lewiston.

## Slide 7: Thresholds for sediment mobility
Definition: Mobility thresholds occur at the exact point when a piece of sediment moves.
Objective: Maintain the ratio of forces that drive and resist movement of the median bedload grain diameter to between 0.025 and 0.085.
Justification: Within these ratios, the bed is neither overly mobile (indicating bed may be composed of overly small grains and/or an over supply of sediment) nor overly stable, which can indicate the opposite.
Frequency and domain for evaluation: When sediment transport monitoring occurs at Douglas City, Limekiln Gulch, and Lewiston.

## Slide 8: Bed mobility and scour
Definition: Bed mobility is sediment movement and scour is sediment movement to depths in the river bed.
Objective: a) Increase bed mobility and scour at a given discharge and b) mobilize the grain size that is coarser than 84% of particles (D84) on bar surfaces at discharges greater than 6000 cfs.
Justification: The increased bed mobility and scour will help create channel complexity and habitat availability and quality. Mobilizing D84s on bars will prevent riparian encroachment.
Frequency and domain for evaluation: For bed mobility, when sediment transport monitoring occurs at Douglas City, Limekiln Gulch, and Lewiston. For scour, in normal and wetter water years on active bars in the restoration reach.