## Slide 1: Trinity River Division Re-Consultation Attributes of a Healthy River
(As presented by)
Eric Peterson
TRRP Science Coordinator

## Slide 2: Where is this presentation heading?
Re-consultation efforts of Joint Leads and collaborators
Overview of Alternatives
Overview of Healthy River Attributes
  a primary method of evaluating the alternatives
  How attributes have evolved since 2000 EIS
How to understand the evaluation pathway
  So that you can provide effective review!

## Slide 3: Thank you, Joint-Leads and collaborators!
Joint-Leads
  Hoopa Valley Tribe
  Yurok Tribe
Collaborators
  NMFS
  USFWS
  CDFW
Accumulated a pile of solid information that will promote change for the better!

## Slide 4
Joint-Leads Review
Cooperating Agency Draft

## Slide 5: This presentation covers a draft in motion
Still some discussion on suite of alternatives
For analysis of alternatives
  40 water years (1981-2020) with climate adjustment to ~2022
  Currently baseflows + restoration flows
    THESE WILL CHANGE to include LKR FAR and Safety-of-Dams
    Metrics will need recalculation
  Also, summarization of metrics is somewhat ad hoc.
    Exact methodology likely to change
    But… overall patterns among alternatives are unlikely to change.

## Slide 6: The Alternatives
NAA (No Action Alternative)
Alt 1: Water Quality Control Plan
Alt 2: Multi-Agency Deliberation
  Method A
  Method B
Alt 3: Modified Natural Hydrograph (oscillating baseflows)
Alt 4: Risk-Informed Operations
Alt 5
Alt 6: Trinity County Local Alternative
Alt 7: Maximum Flow

## Slide 7: No Action Alternative
2000 ROD
Accommodates WVF, dependent on AM (but analyzed without)
Planning minimum pool: 600,000 AF

## Slide 8: Alternative 1 Water Quality Control Plan
CVPIA minimum volume 340,000 AF every year
Leaves 91,000 AF above baseflows for AM
Planning minimum pool: none

## Slide 9
2000 ROD Volumes
Decision tree like WVF but more water for Sync Flows
Planning minimum pools:
  1,200,000 AF
  900,000 AF
  750,000 AF
Alternative 2
Multi-Agency Deliberation (Method A)

## Slide 10
2000 ROD Volumes
Algorithmic flow scheduling based on Salmon River at Somes Bar
Planning minimum pools:
  1,200,000 AF
  900,000 AF
  750,000 AF
Alternative 2 Multi-Agency Deliberation (Method B)

## Slide 11
2000 ROD Volumes but shifted April to April
Baseflows vary, and can be lower in summer (CritDry = 300 cfs)
Variable volume for AM peak
Planning minimum pools:
  1,200,000 AF
  900,000 AF
  750,000 AF
Alternative 3
Modified Natural Hydrograph
(Oscillating Baseflows)

## Slide 12
Restoration flows like Alt 2 except: 15% cut to ROD volumes in consecutive dry years plus first year afterward
Planning minimum pool: 750,000 AF
Alternative 4
Risk-Informed Operations
(as represented with Method A)

## Slide 13
Higher minimum pool, slower reduction
2000 ROD Volumes except: 200,000 AF held back in first wet year after drought with missed pool levels
That held volume may be scheduled by AM the subsequent 3 years
AM limited to NAA
Alternative 6
Trinity County Local Alternative
Planning minimum pools:
  1,500,000
  1,300,000
  1,100,000
  1,000,000
  900,000
  825,000
  750,000

## Slide 14
Target 70% inflows to river
Algorithmic based on TR above Coffee Creek gage
With low pool levels, summer baseflows can drop as low as 100cfs (40 year modeling never went under 150cfs)
Planning minimum pool:
Alternative 7
Maximum Flow

## Slide 15: EIS 2000 – Healthy Rivers
10 Fluvial River Attributes
1 Salmonid Temperature Attribute
Evaluation:
Only release schedules (no SOD)
Flow Thresholds and SNTEMP
Scored 0, 1, 2 for each of 37 attribute objectives, then summed
Further estimation of index of spawner population for comparing alternatives
Appendix B

## Slide 16: Revision of Attributes
Spatially complex channel geomorphology
Flows and water quality are predictably unpredictable
Frequently mobilized channelbed surface
Periodic channelbed scour and fill
Balanced fine and coarse sediment budgets
Periodic channel migration
A functional floodplain
Infrequent channel resetting floods
Self-sustaining diverse riparian plant community
Naturally fluctuating groundwater table
Water temperature and microhabitat
Spatially complex channel geomorphology
Flows are variable and synchronized with tributaries
Frequently mobilized channelbed surface at appropriate time synchronized with tributaries to support geomorphic function and ecosystem health (winter months)
Periodic channelbed scour and fill at appropriate time synchronized with tributaries to support species and ecosystem health (winter months)
Maintain appropriate grain size distribution in the bedload
Periodic channel migration
Functional floodplain
Self-sustaining diverse riparian plant communities
Water temperature and microhabitat
X
X
31 Objectives Total (22 currently evaluated)
37 Objectives Total

## Slide 17: Revision of Attributes
Spatially complex channel geomorphology
Flows and water quality are predictably unpredictable
Frequently mobilized channelbed surface
Periodic channelbed scour and fill
Balanced fine and coarse sediment budgets
Periodic channel migration
A functional floodplain
Infrequent channel resetting floods
Self-sustaining diverse riparian plant community
Naturally fluctuating groundwater table
Water temperature and microhabitat
Spatially complex channel geomorphology
Flows are variable and synchronized with tributaries
Frequently mobilized channelbed surface at appropriate time synchronized with tributaries to support geomorphic function and ecosystem health (winter months)
Periodic channelbed scour and fill at appropriate time synchronized with tributaries to support species and ecosystem health (winter months)
Maintain appropriate grain size distribution in the bedload
Periodic channel migration
Functional floodplain
Self-sustaining diverse riparian plant communities
Water temperature and microhabitat
X
X
Original Attribute 8, “Infrequent channel resetting floods,” has been removed, as these events are largely beyond management control and the attribute lacked spatial specificity. The intended function of these high-magnitude flows—such as broad sediment redistribution and channel resetting—can be more effectively addressed elsewhere, recognizing that these flows may not occur system-wide at the same time, but should occur somewhere within the system with that frequency.
Additionally, it was recognized that releasing 11,000 cfs from Lewiston Dam too frequently can lead to undesirable bed armoring and fossilization, particularly in the absence of adequate fine sediment inputs. This underscores the importance of balancing flow magnitude with sediment availability.

## Slide 18: Revision of Attributes
Spatially complex channel geomorphology
Flows and water quality are predictably unpredictable
Frequently mobilized channelbed surface
Periodic channelbed scour and fill
Balanced fine and coarse sediment budgets
Periodic channel migration
A functional floodplain
Infrequent channel resetting floods
Self-sustaining diverse riparian plant community
Naturally fluctuating groundwater table
Water temperature and microhabitat
Spatially complex channel geomorphology
Flows are variable and synchronized with tributaries
Frequently mobilized channelbed surface at appropriate time synchronized with tributaries to support geomorphic function and ecosystem health (winter months)
Periodic channelbed scour and fill at appropriate time synchronized with tributaries to support species and ecosystem health (winter months)
Maintain appropriate grain size distribution in the bedload
Periodic channel migration
Functional floodplain
Self-sustaining diverse riparian plant communities
Water temperature and microhabitat
X
X
Original Attribute 10 “Naturally fluctuating groundwater table” removed.
Groundwater monitoring with piezometers at Channel Rehabilitation sites has demonstrated that groundwater elevation is almost uniformly tied to river surface elevation even where groundwater temperature suggests lateral inflow (1 exception at Lowden Ranch). Groundwater would also not differ in bedrock confined reaches. Thus TRRP has concluded that groundwater largely does not fluctuate independently of river discharge.

## Slide 19: Quantitative Evaluation

## Slide 20: Quantitative Evaluation
Datasets
Constructed hydrographs
  40 years
  WY 1981-2020
  updated climate to ~2022
Metrics
Target thresholds (like in 2000)
  Frequencies
Frequency of peaks
Correlations to Salmon River
Coefficient of Variation
Inundation Duration
Baseflow Index
Richardson Baker Flashiness Index
Recession Rate
Many are from Yarnell et al. (2020)
7 Attributes 22 Objectives

## Slide 21: Diving in…. Results and Interpretation
Lots of Tables
Summarized by Color Coding
  Placeholder method
  Red = poor performance
  Yellow = weak
  Green = moderate
  Blue = good
  Purple = overshot
    Usually to a not-good degree

## Slide 22: Attribute 2: Flows are variable and synchronized with tributaries.
Objective 2.1 summer baseflow variation
Objective 2.2 winter baseflow variation
Objective 2.3 winter peak flow variation synchronized
Objective 2.4 snowmelt peak flow variation synchronized
Objective 2.5 snowmelt recession synchronized
Evaluation illustrated by Attribute 2

## Slide 23: Attribute 2: Flows are variable and synchronized with tributaries.
Objective 2.1 summer baseflow variation
Objective 2.2 winter baseflow variation
Objective 2.3 winter peak flow variation synchronized
Objective 2.4 snowmelt peak flow variation synchronized
Objective 2.5 snowmelt recession synchronized
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Baseflow Index | 0.39 | 0.64 | 0.39 | 0.39 | 0.47 | 0.40 | 0.38 | 0.22 | 0.03
Correlation with Salmon River, Jul-Sept | 0.61 | - | 0.63 | 0.10 | 0.38 | 0.63 | 0.61 | 0.72 | 1.00
Summary |  |  |  |  |  |  |  |  | 

## Slide 24: Attribute 2: Flows are variable and synchronized with tributaries.
Objective 2.1 summer baseflow variation
Objective 2.2 winter baseflow variation
Objective 2.3 winter peak flow variation synchronized
Objective 2.4 snowmelt peak flow variation synchronized
Objective 2.5 snowmelt recession synchronized
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Coefficient of Variation, Jan-Mar | 0.00 | 0.00 | 1.09 | 0.96 | 0.22 | 1.09 | 0.00 | 0.89 | 0.95

## Slide 25: Attribute 2: Flows are variable and synchronized with tributaries.
Objective 2.1 summer baseflow variation
Objective 2.2 winter baseflow variation
Objective 2.3 winter peak flow variation synchronized
Objective 2.4 snowmelt peak flow variation synchronized
Objective 2.5 snowmelt recession synchronized
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Flashiness | 0.04 | 0.03 | 0.11 | 0.11 | 0.05 | 0.11 | 0.04 | 0.16 | 0.18
Correlation with SR Oct-Mar | -0.21 | -0.21 | 0.47 | 0.92 | 0.31 | 0.47 | -0.21 | 0.89 | 1.00
Summary |  |  |  |  |  |  |  |  | 

## Slide 26: Attribute 2: Flows are variable and synchronized with tributaries.
Objective 2.1 summer baseflow variation
Objective 2.2 winter baseflow variation
Objective 2.3 winter peak flow variation synchronized
Objective 2.4 snowmelt peak flow variation synchronized
Objective 2.5 snowmelt recession synchronized
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Correlation with SR Apr-May | 0.05 | 0.01 | 0.26 | 0.64 | 0.16 | 0.26 | 0.00 | 0.88 | 1.00

## Slide 27: Attribute 2: Flows are variable and synchronized with tributaries.
Objective 2.1 summer baseflow variation
Objective 2.2 winter baseflow variation
Objective 2.3 winter peak flow variation synchronized
Objective 2.4 snowmelt peak flow variation synchronized
Objective 2.5 snowmelt recession synchronized
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
dQ/dt correlation to SR May-Jun | 0.07 | -0.02 | -0.03 | 0.62 | -0.04 | -0.02 | 0.06 | 0.85 | 1.00

## Slide 28: Attribute 2: Flows are variable and synchronized with tributaries.
dQ/dt correlation to SR May-Jun | 0.07 | -0.02 | -0.03 | 0.62 | -0.04 | -0.02 | 0.06 | 0.85 | 1.00
Correlation with SR Apr-May | 0.05 | 0.01 | 0.26 | 0.64 | 0.16 | 0.26 | 0.00 | 0.88 | 1.00
Flashiness | 0.04 | 0.03 | 0.11 | 0.11 | 0.05 | 0.11 | 0.04 | 0.16 | 0.18
Correlation with SR Oct-Mar | -0.21 | -0.21 | 0.47 | 0.92 | 0.31 | 0.47 | -0.21 | 0.89 | 1.00
Coefficient of Variation, Jan-Mar | 0.00 | 0.00 | 1.09 | 0.96 | 0.22 | 1.09 | 0.00 | 0.89 | 0.95
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Baseflow Index | 0.39 | 0.64 | 0.39 | 0.39 | 0.47 | 0.40 | 0.38 | 0.22 | 0.03
Correlation with Salmon River, Jul-Sept | 0.61 | - | 0.63 | 0.10 | 0.38 | 0.63 | 0.61 | 0.72 | 1.00
4 R 1 Y
5 R
1 R 2 Y
1 G
1 B
1 R
4 B
3 R 2 Y
1 R 2 Y
1 G
1 B
4 R 1 Y
5 B

## Slide 29: Alternatives
NAA (No Action Alternative)
Alt 1: Water Quality Control Plan
Alt 2: Multi-Agency Deliberation
  Method A
  Method B
Alt 3: Modified Natural Hydrograph (oscillating baseflows)
Alt 4: Risk-Informed Operations
Alt 6: Trinity County Local Alternative
Alt 7: Maximum Flow

## Slide 30: No Action Alternative
Of 22 Objectives evaluated
  17 R
  3 Y
  1 G (6.1 channel migration: frequency of peaks > 8500 cfs)
  1 B (8.4 seed germination: frequency flows for 21 days in May-June)
Some correlations to Salmon River not calculable due to lack of variation in time periods

## Slide 31: Alt 1 Water Quality Control Plan
Of 22 Objectives evaluated
  21 R
  1 Y
A majority of flow thresholds are never met
Some correlations to Salmon River not calculable due to lack of variation in time periods
Relative to NAA: poor performance

## Slide 32: Alt 2 Multi-Agency Deliberation (Method A)
Of 22 Objectives evaluated
  2 R
  10 Y
  8 G
  2 B
Relative to NAA: substantial improvement

## Slide 33: Alt 2 Multi-Agency Deliberation (Method B)
Of 22 Objectives evaluated
  2 R
  6 Y
  9 G
  5 B
Relative to NAA: substantial improvement

## Slide 34: Alt 3: Modified Natural Hydrograph (Oscillating Baseflows)
Of 22 Objectives evaluated
  10 R
  9 Y
  3 G
  0 B
Relative to NAA: slight improvement

## Slide 35: Alt 4 Risk-Informed Operations (as represented with Method A)
Of 22 Objectives evaluated
  2 R
  10 Y
  8 G
  2 B
Same as Alt 2 method A
  Zoom into the metric values and there are small differences
Relative to NAA: substantial improvement

## Slide 36: Alt 6: Trinity County Local Alternative
Of 22 Objectives evaluated
  17 R
  4 Y
  1 P
Relative to NAA: few differences

## Slide 37: Alt 7 Maximum Flow
Of 22 Objectives evaluated
  0 R
  1 Y
  2 G
  16 B
  3 P
Relative to NAA: a ‘flood’ of improvements (best performing Alt)

## Slide 38: Ranking: most functional to least functional
Alt 7
Alt 2 method B
Alt 2 method A
Alt 4 almost matched
Alt 3
Alt 6
NAA
Alt 1

## Slide 39: Extras

## Slide 40: Attribute 3: Frequently mobilized channelbed surface at appropriate time synchronized with tributaries to support geomorphic function and ecosystem health (winter months).
2 R
2 R
2 Y
2 Y
2 R
2 Y
2 R
1 G 1 B
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Threshold 4500 cfs | 88% * | 0% | 75% | 55% | 88% | 75% | 78% * | 90% | 93%
Correlation to SR Dec-Feb | - | - | 0.46 | 0.94 | 0.09 | 0.46 | - | 0.87 | NA
Threshold 6000 cfs | 60% | 0% | 58% | 30% | 60% | 55% | 58% | 78% | 90%
Correlation to SR Dec-Feb | - | - | 0.46 | 0.94 | 0.09 | 0.46 | - | 0.87 | NA

## Slide 41: Attribute 4: Periodic channelbed scour and fill at appropriate time synchronized with tributaries to support species and ecosystem health (winter months).
3 R (1 P)
3 R
3 Y
1 Y
1 G 1 B
3 R (1 P)
2 Y
3 R
(2 P)
3 B
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Threshold 8500 cfs | 43% | 0% | 25% | 15% | 43% | 23% | 28% | 58% | 78%
Correlation to SR Dec-Feb | - | - | 0.46 | 0.94 | 0.09 | 0.46 | - | 0.87 | NA
Threshold 10,500 cfs | 13% | 0% | 5% | 8% | 13% | 5% | 8% | 45% | 65%
Correlation to SR Dec-Feb | - | - | 0.46 | 0.94 | 0.09 | 0.46 | - | 0.87 | NA
TBD? |  |  |  |  |  |  |  |  | 
Correlation to SR Dec-Feb | - | - | 0.46 | 0.94 | 0.09 | 0.46 | - | 0.87 | NA

## Slide 42: Attribute 5: Maintain appropriate grain size distribution in the bedload.
1 R 1 Y
2 R
1 G
1 B
1 Y
1 G
2 Y
1 G
1 B
1 R 1 Y
1 G 1 B
Fine Sediment: No basis for evaluation.
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Coefficient of Variation among flow peaks. | 0.33 | 0.00 | 0.83 | 0.61 | 0.35 | 0.82 | 0.34 | 0.67 | 0.97
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Threshold 4500 cfs | 88% | 0% | 75% | 55% | 88% | 75% | 78% | 90% | 93%
Correlation to SR Year-Round | 0.12 | 0.07 | 0.40 | 0.81 | 0.26 | 0.40 | 0.11 | 0.90 | 1.00

## Slide 43: Attribute 6: Periodic channel migration.
1 G
1 R
1 Y
1 R
1 G
1 Y
1 Y
1 B
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Mean number of Peaks >= 8500 cfs per year | 0.43 | 0.00 | 0.25 | 0.15 | 0.43 | 0.23 | 0.30 | 1.45 | 2.15

## Slide 44: Attribute 7: Functional Floodplain
3 R 1 Y
3 R
1 Y
1 Y/P
3 G
4 G/P
1 R/P 1 Y
2G
1 Y/P
3 G
3 R/P 1 Y
4 B/P
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7
Inundation Acre-Days Year-Round | (881,571) 1,743,868 (2,537,327) | (691,557) 693,043 (697,501) | (936,020) 2,500,528 (4,488,263) | (878,082) 2,746,464 (4,694,403) | (1,470,256) 2,521,522 (3,342,305) | (711,149) 2,469,339 (4,488,263) | (881,571) 1,718,583 (2,665,116) | (2,836,389) 10,625,047 (22,814,324)
Correlation to SR Year-Round | 0.12 | 0.07 | 0.40 | 0.81 | 0.26 | 0.40 | 0.11 | 0.90
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Threshold 4500cfs | 88% | 0% | 75% | 55% | 88% | 75% | 78% | 90% | 93%
Correlation to SR Jan-Mar | - | - | 0.31 | 0.93 | 0.04 | 0.31 | - | 0.84 | 1.00
Correlation to SR Apr-May | 0.05 | 0.01 | 0.26 | 0.64 | 0.16 | 0.26 | 0.00 | 0.88 | 
Inundation Acre-Days at 10-week duration, Jan-Apr | (0) 0 (0)* | (0) 0 (0)* | (0) 212 (496) | (0) 231 (815) | (142) 249 (292) | (0) 209 (496) | (0) 0 (0)* | (278) 1,143 (2,300)
Inundation Acre-Days, Jan-Apr | (61,682) 62,019 (62,827) | (63,251) 63,404 (63,861) | (64,542) 69,799 (76,318) | (62,240) 69,557 (79,746) | (67,765) 72,054 (76,469) | (64,517) 69,701 (76,318) | (61,590) 62,041 (63,058) | (74,532) 91,504 (113,441)

## Slide 45: Attribute 8: Self-sustaining diverse riparian plant communities.
4 R
1 B
5 R
1 R 1 Y
3 G
2 Y
3 G
1 R 4 Y
1 R 1 Y
3 G
4 R 1 P
1 Y
4 B
Metric | NAA | Alt 1 | Alt 2a | Alt 2b | Alt 3 | Alt 4 | Alt 6 | Alt 7 | SR
Threshold 6000 cfs | 60% | 0% | 58% | 30% | 60% | 55% | 58% | 78% | 90%
Correlation to SR Year-Round | 0.12 | 0.07 | 0.40 | 0.81 | 0.26 | 0.40 | 0.11 | 0.90 | 1.00
Threshold 8500 cfs | 43% | 0% | 25% | 15% | 43% | 23% | 28% | 58% | 78%
Correlation to SR Year-Round | 0.12 | 0.07 | 0.40 | 0.81 | 0.26 | 0.40 | 0.11 | 0.90 | 1.00
Threshold 10,500 cfs | 13% | 0% | 5% | 8% | 13% | 5% | 8% | 45% | 65%
Correlation to SR Year-Round | 0.12 | 0.07 | 0.40 | 0.81 | 0.26 | 0.40 | 0.11 | 0.90 | 1.00
Frequency of years with 21 days of 1700-4500 in May and June | 75% | 0% | 3% | 35% | 0% | 3% | 85% | 25% | 50%
Coefficient of Variation, May-Sept | 1.19 | 0.35 | 0.63 | 0.86 | 0.48 | 0.63 | 1.16 | 1.40 | 1.19
Correlation to SR Year-Round | 0.12 | 0.07 | 0.40 | 0.81 | 0.26 | 0.40 | 0.11 | 0.90 | 1.00

## Slide 46: Attribute 9: Flow sufficient to meet State Water Resources Control Board temperature objectives under all conditions.
TBD