## Slide 1: 2024 Restoration Reach Vegetation Map
Applied River Sciences: F. Horobin
Hoopa Valley Tribe
May 4, 2026

## Slide 2: 13 Geomorphic reaches
Based on tributary confluences, valley width, and slope changes in the longitudinal profile (Curtis et al., 2015 ; HVT & MA, 2015).
Expectations
Geomorphic control on vegetation patterns
  Upstream–downstream variation driven by reach type
Constrained vs. unconfined reaches
  Narrow/geomorphically restricted → ↓ riparian cover (scour, drought, urban pressure)
  Wide alluvial valleys → ↑ potential for riparian expansion
  Urban/upland boundaries → limit future colonization
Restoration trade-offs
  Channel widening & floodplain connectivity
  ↓ vegetation in some areas ↔ ↑ open water
Predicted trend
  Largest gains expected in alluvial reaches (Dutch Creek → North Fork)
Hoopa Valley Tribe
Vegetation mapping conducted every ~5 yrs since 2003 to track long-term response to restoration actions
Recent disturbances include the 2017 Helena Fire and 2021 Monument Fire, plus severe droughts in WY 2013-2015, 2018, and 2020-2022

## Slide 3: Study Objectives
2024 Mapping Study Objectives
Map all vegetated and unvegetated areas in the
Restoration Reach using current aerial imagery
Quantify changes in riparian abundance, diversity,
and composition:
  2003 - 2024
  2014 -2024
Evaluate the success of core objectives:
  1) Riparian vegetation will be more abundant following implementation of ROD management actions.
  2) Riparian plantings on existing and constructed floodplains will maintain or increase established vegetation.
  3) Native riparian vegetation will be more diverse following implementation of ROD management actions.
Hoopa Valley Tribe

## Slide 4: Methods & Classification
Cover types were mapped based on prior established cover rules
  Dominant species or community
Hoopa Valley Tribe
Attributes were assigned to each cover type polygon:
  Functional group (10), Upland, Riparian, Wetland, Invasive Riparian etc.)
  Structure (Herb, Tree, Shrub)
  Life-Origin (Native, Non-native, Invasive)
  Sensitive Natural Community
  Fish Habitat (at 2ft inundation)
  ___________?

## Slide 5: Mapping Boundaries
2003 mapping boundary ~4,806 ac
  Used for functional group comparisons for every 5yr mapping event
  500-m from channel centerline or
  10-m above the centerline or
  ESL extent in 2003
4
Hoopa Valley Tribe
2024 mapping extent ~8,074 ac
  Extended to edges of aerial photos
  Mapped beyond current channel rehabilitation site Environmental Study Limits (ESLs)
  Used for comparing 5 yr mapping events at channel rehabilitation sites

## Slide 6
2024 Mapping Study Objectives
Evaluate the success of core objectives:
  1) Riparian Area: Riparian vegetation will be more abundant following implementation of ROD management actions.
  2) Riparian plantings on existing and constructed floodplains will maintain or increase established vegetation.
  3) Diversity: Native riparian vegetation will be more diverse following implementation of ROD management actions.
Hoopa Valley Tribe

## Slide 7: Total Riparian cover
Hoopa Valley Tribe
Total riparian: +50 ac since 2003
Last decade: +60 ac (2014-2024)
Chart: Area (acres)
| 2003 | 2010 | 2014 | 2019 | 2024
Combined Riparian | 979.2786 | 955.3094 | 969.8886 | 946.4136 | 1029.6805
Year | 2003 | 2010 | 2014 | 2019 | 2024 | Change since ‘03
Grand Total | 979.3 | 955.3 | 969.9 | 946.4 | 1029.7 | 50.4

## Slide 8: Change by Reach
Results
Geomorphically confined reaches (e.g., Dutton Creek–Dutch Creek)
  Observed ↓ in riparian cover
  Likely driven by scour + drought + urban influence
Total increase is spread out amongst other reaches
Reach | Total Riparian acres mapped |  |  |  |  |  | 
 | 2003 | 2010 | 2014 | 2019 | 2024 | Area change since 2003 | Area change since 2014
Lewiston–Deadwood | 15.8 | 15.1 | 17.8 | 19.3 | 19.2 | 3.4 | 1.4
Deadwood–Rush Creek | 93.7 | 85.3 | 83.5 | 89.0 | 95.4 | 1.8 | 11.9
Rush Creek–Trinity House Gulch | 119.1 | 119.4 | 122.6 | 126.8 | 138.9 | 19.8 | 16.3
Trinity House Gulch–Limekiln Gulch | 43.5 | 41.3 | 38.3 | 37.1 | 39.7 | -3.8 | 1.4
Limekiln Gulch–Vitzthum Gulch | 67.0 | 68.2 | 74.9 | 73.4 | 76.9 | 10.0 | 2.0
Vitzthum Gulch–Reading Creek | 117.1 | 104.3 | 111.0 | 112.9 | 114.6 | -2.5 | 3.7
Reading Creek–Dutton Creek | 93.4 | 84.3 | 85.5 | 85.3 | 101.2 | 7.8 | 15.7
Dutton Creek–Dutch Creek | 40.3 | 41.3 | 39.8 | 37.3 | 37.7 | -2.6 | -2.1
Dutch Creek–Oregon Gulch | 185.1 | 190.0 | 198.7 | 186.3 | 187.8 | 2.7 | -10.9
Oregon Gulch–Canyon Creek | 53.4 | 54.6 | 50.7 | 47.0 | 55.1 | 1.8 | 4.5
Canyon Creek–McCartney's Pond | 59.6 | 59.1 | 52.9 | 51.9 | 64.1 | 4.6 | 11.2
McCartney's Pond–Lime Point | 56.1 | 58.6 | 61.0 | 47.2 | 55.3 | -0.8 | -5.8
Lime Point–North Fork Trinity River | 35.3 | 34.1 | 33.4 | 33.1 | 43.9 | 8.5 | 10.5
Grand Total | 979.3 | 955.3 | 969.9 | 946.4 | 1029.7 | 50.4 | 59.8
Hoopa Valley Tribe

## Slide 9: Systemwide Changes
Vegetation shifts under:
  Restoration flows, channel rehab, sediment management
  Fire, drought, and urbanization
Native vs. Total Riparian
“No net loss” includes:
  riparian
  invasive riparian
  wetland
Functional Group | 2003 (ac) | 2010 (ac) | 2014 (ac) | 2019 (ac) | 2024 (ac) | Change since 2003 (ac) | Change since 2014 (ac)
Annual grassland | 678.6 | 661.0 | 870.7 | 793.2 | 746.0 | 67.5 | -124.7
Burned | 0 | 0 | 0 | 103.3 | 0 | 0 | 0
Human disturbance | 772.2 | 794.7 | 554.6 | 600.0 | 706.7 | -65.5 | 152.1
Invasive riparian | 28.4 | 20.5 | 88.5 | 83.3 | 111.7 | 83.3 | 23.2
Invasive upland | 16.3 | 13.3 | 7.7 | 10.1 | 39.1 | 22.7 | 31.3
Open | 348.9 | 322.7 | 336.1 | 350.4 | 304.4 | -44.5 | -31.8
Open water | 418.8 | 457.4 | 456.3 | 483.1 | 489.4 | 70.6 | 33.1
Perennial grassland | 0 | 2.0 | 21.5 | 13.6 | 18.1 | 18.1 | -3.5
Riparian | 931.8 | 919.2 | 871.5 | 853.5 | 899.5 | -32.3 | 28.0
Unknown | 97.4 | 88.2 | 0 | 5.4 | 0 | -97.4 | 0
Upland | 1594.5 | 1611.4 | 1688.7 | 1600.5 | 1572.6 | -21.9 | -116.0
Wetland | 19.0 | 15.6 | 10.1 | 9.6 | 18.4 | -0.6 | 8.3
Grand Total | 4905.9 | 4905.9 | 4905.9 | 4905.9 | 4905.9 |  | 
Hoopa Valley Tribe

## Slide 10: Fire and Riparian Vegetation

## Slide 11: 2017 Helena and 2021 Monument Fires
Native riparian:
Largest decrease: Oregon Gulch – Canyon Creek - 4.2 ac
  Most likely due to Oregon Gulch CRS construction
Overall Trend: Native Riparian
-3.0 ac after 3 yrs
Fire | Acres within Restoration Reach | Total Acres Burned
2017 Helena | 542 | 21,846
2021 Monument | 201 | 223,124
Both Fires | 27 | 3,501
Fire intensity varied within perimeters
2017 Helena Fire : ~7 yrs of recovery
Hoopa Valley Tribe
Native riparian:
Largest decrease: McCartney’s Pond – Lime Point -6.7 ac
2019-2024
Overall Trend: Native riparian
+1.5 ac after 2 yrs, -1.6 ac after 7 yrs
2021 Monument Fire : ~ 3yrs of recovery
Notes: ~27 acres were burn in both fires, mainly within the Lime Point – North Fork Trinity River

## Slide 12: 2017 Helena Fire
Functional group | 2017 Helena Fire Perimeter Pre- and Post-burn Changes (acres) |  |  |  |  |  |  |  |  |  |  | 
 | Canyon Creek–McCartney’s Pond |  |  | McCartney’s Pond–Lime Point |  |  | Lime Point–North Fork Trinity River |  |  | Total |  | 
Map Year | 2014 | 2019 | 2024 | 2014 | 2019 | 2024 | 2014 | 2019 | 2024 | 2014 | 2019 | 2024
Annual grassland | 14.9 | 11.1 | 13.2 | 63.6 | 43.5 | 74.6 | 24.1 | 24.5 | 29.0 | 102.6 | 79.1 | 116.8
Perennial grassland | 0 | 0 | 0 | 0.6 | 1.4 | 2.2 | 0 | 0.1 | 0.04 | 0.6 | 1.5 | 2.2
Human disturbance | 8.6 | 11.2 | 11.1 | 43.0 | 80.6 | 71.1 | 11.0 | 11.1 | 13.2 | 62.7 | 102.9 | 95.3
Invasive riparian | 0.2 | 0.5 | 2.0 | 10.7 | 8.5 | 10.5 | 3.9 | 3.9 | 7.5 | 14.9 | 12.9 | 20.0
Invasive upland | 0.4 | 0.5 | 1.5 | 5.0 | 4.8 | 21.7 | 0.5 | 0.4 | 1.8 | 5.9 | 5.6 | 25.0
Open | 8.9 | 10.8 | 9.0 | 33.1 | 22.9 | 33.6 | 5.0 | 5.3 | 5.8 | 47.1 | 39.0 | 48.4
Open water | 5.9 | 5.9 | 5.8 | 29.0 | 28.9 | 27.7 | 13.1 | 13.7 | 13.9 | 47.9 | 48.5 | 47.4
Riparian | 11.4 | 11.4 | 11.3 | 50.3 | 51.3 | 44.6 | 17.4 | 17.9 | 22.1 | 79.1 | 80.6 | 78.0
Upland | 29.0 | 27.8 | 25.2 | 99.0 | 92.5 | 48.3 | 52.7 | 50.9 | 34.3 | 180.6 | 171.2 | 107.8
Wetland | 0.02 | 0 | 0.2 | 0.03 | 0.02 | 0.13 | 0 | 0 | 0.1 | 0.1 | 0.02 | 0.4
Total | 79.3 | 79.3 | 79.3 | 334.5 | 334.5 | 334.5 | 127.7 | 127.7 | 127.7 | 541.5 | 541.5 | 541.5
~7 yrs of post-fire recover
Hoopa Valley Tribe
Native riparian:
Largest decrease: McCartney’s Pond – Lime Point -6.7 ac
2019-2024
Overall Trend: Native riparian
+1.5 ac after 2 yrs, -1.6 ac after 7 yrs

## Slide 13: 2021 Monument Fire
Functional group | 2021 Monument Fire Perimeter Pre- and Post-burn Changes (acres) |  |  |  |  |  |  |  | 
 | Oregon Gulch - Canyon Creek |  | Canyon Creek - McCartney's Pond |  | Lime Point–North Fork Trinity River |  | Total |  | 
Map Year | 2019 | 2024 | 2019 | 2024 | 2019 | 2024 | 2019 | 2024 | Total Change
Annual grassland | 28.8 | 27.2 | 8.6 | 6.6 | 4.9 | 11.2 | 42.2 | 45.0 | 2.8
Perennial grassland | 0.0 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.10
Human disturbance | 24.8 | 26.5 | 3.7 | 2.3 | 0.1 | 0.0 | 28.6 | 28.8 | 0.2
Invasive riparian | 2.0 | 8.2 | 0.2 | 0.3 | 1.1 | 2.8 | 3.3 | 11.3 | 8.0
Invasive upland | 1.5 | 2.2 | 0.2 | 0.6 | 0.0 | 0.0 | 1.7 | 2.8 | 1.1
Open | 17.5 | 20.8 | 7.5 | 9.1 | 3.7 | 1.7 | 28.8 | 31.6 | 2.8
Open water | 11.8 | 12.6 | 2.8 | 2.7 | 0.6 | 0.6 | 15.2 | 16.0 | 0.8
Riparian | 21.1 | 16.9 | 2.9 | 2.6 | 6.7 | 8.1 | 30.7 | 27.7 | -3.0
Upland | 23.5 | 16.0 | 5.5 | 7.0 | 21.7 | 14.4 | 50.6 | 37.4 | -13.2
Wetland | 0.2 | 0.6 | 0.0 | 0.0 | 0.0 | 0.0 | 0.2 | 0.6 | 0.4
Total | 131.2 | 131.2 | 31.3 | 31.3 | 38.8 | 38.8 | 201.2 | 201.2 | 
~3 yrs of post-fire recovery
Hoopa Valley Tribe
Native riparian:
Largest decrease: Oregon Gulch – Canyon Creek - 4.2 ac
  Most likely due to Oregon Gulch CRS construction
Overall Trend: Native Riparian
-3.0 ac after 3 yrs

## Slide 14: Spatial Distribution of Combined Rip. Veg
Hoopa Valley Tribe
No Change

## Slide 15
2024 Mapping Study Objectives
Evaluate the success of core objectives:
  1) Riparian Area: Riparian vegetation will be more abundant following implementation of ROD management actions.
  2) Riparian plantings on existing and constructed floodplains will maintain or increase established vegetation.
  3) Diversity: Native riparian vegetation will be more diverse following implementation of ROD management actions.
Hoopa Valley Tribe

## Slide 16: Riparian Vegetation Area Change within Each ESL
 | Riparian + invasive riparian + wetland functional group areas (acres) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Construction Date
 | 2003 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2014 | 2015 | 2016 | 2017 | 2019 | 2024 | 
Hatchery | 2.2 | – | – | – | – | – | – | – | – | – | – | 15.1 | 15.1 | 14.8 | 15.3 | Not constructed
Lewiston Hatchery CSA | 2.0 | – | – | 0.7 | 1.2 | – | – | – | – | 1.5 | 2.0 | 2.0 | 2.0 | 2.0 | 1.7 | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Not constructed
Lewiston Four1 | 38.8 | – | 38.5 | 38.5 | 35.1 | 33.4 | 37.1 | 36.6 | – | 34.3 | 36.1 | 36.1 | 36.1 | 36.3 | 39.5 | 2008
Sawmill | 28.2 | – | – | 28.4 | 30.1 | – | 24.0 | 24.2 | 25.9 | 25.7 | 27.7 | 28.2 | 28.2 | 28.7 | 32.9 | 2009
Upper Rush Creek | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 23.5 | Not constructed
Lower Rush Creek | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 28.4 | Not constructed
Dark Gulch | 35.1 | – | 35.6 | 35.6 | 34.6 | 32.6 | 36.8 | 35.6 | 36.3 | 36.1 | 36.1 | 32.4 | 32.9 | 32.6 | 39.0 | 2008
Bucktail 2016 | 18.3 | – | – | – | – | – | 21.5 | – | – | 22.2 | 23.7 | 19.5 | 20.0 | 19.8 | 25.7 | 2016
Lowden Meadows | 35.8 | – | – | – | 53.1 | 52.1 | 52.1 | 48.7 | – | 53.1 | 54.4 | 54.6 | 56.8 | 59.6 | 66.2 | 2010
Trinity House Gulch | 12.4 | – | – | – | – | – | 13.1 | 9.1 | – | 10.9 | 11.4 | 11.9 | 12.1 | 13.6 | 13.1 | 2010
Tom Lang Gulch | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 5.9 | Not constructed
Poker Bar | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 17.3 | Not constructed
Limekiln Gulch | 14.3 | – | – | – | – | – | 14.3 | – | – | 16.3 | 16.3 | 15.8 | 15.8 | 16.1 | 17.8 | 2015
McIntyre Gulch | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 12.8 | Not constructed
Indian Creek | 83.8 | – | – | 83.5 | 72.6 | 68.7 | 70.4 | 69.4 | – | 74.6 | 77.8 | 78.6 | 79.1 | 78.8 | 82.5 | 2007
Douglas City | 37.3 | – | – | – | – | – | 27.4 | – | – | 38.3 | 37.3 | 37.3 | 37.1 | 39.0 | 44.0 | Construction occurred several times in different parts of the ESL
Reading Creek | 35.3 | – | – | – | 32.9 | – | 27.7 | 26.9 | 41.0 | 32.1 | 32.4 | 32.9 | 32.4 | 32.4 | 34.1 | 2010
Upper Steiner Flat | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 4.9 | Not constructed
Middle Steiner Flat | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 6.9 | Not constructed
Lower Steiner Flat | 19.8 | – | – | – | 19.0 | – | 19.0 | 19.0 | – | 22.5 | 23.0 | 23.2 | 23.0 | 22.5 | 25.2 | 2012
Lorenz Gulch | 19.0 | – | – | – | – | – | 18.0 | – | – | 17.1 | 16.6 | 16.8 | 17.1 | 17.1 | 20.3 | 2013
Dutch Creek | 30.9 | – | – | – | – | – | 30.9 | – | – | 30.9 | 30.9 | 30.9 | 30.9 | 25.7 | 23.7 | 2020
Evans Bar | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 37.8 | Not constructed
Soldier Creek | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 9.6 | Not constructed
Chapman Ranch | 37.1 | – | – | – | – | – | 37.8 | – | – | 37.3 | 38.3 | 38.5 | 43.2 | – | – | Split into two construction phases during design
Chapman Ranch | – | – | – | – | – | – | – | – | – | – | – | – | – | 28.2 | 26.2 | Construction-related impacts in 2019
Phase A |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Chapman Ranch | – | – | – | – | – | – | – | – | – | – | – | – | – | 18.3 | 11.9 | Constructed in 2021
Phase B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Deep Gulch & | 48.4 | – | – | – | – | – | 51.4 | – | – | 55.1 | – | – | – | 52.1 | 60.3 | 2017
Sheridan Creek |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Oregon Gulch | – | – | – | – | – | – | – | – | – | – | – | – | – | 52.9 | 45.2 | 2023
Sky Ranch | – | – | – | – | – | – | – | – | – | – | – | – | – | – | 25.7 | Not constructed
Upper Junction City | 10.1 | – | – | – | 9.6 | 9.6 | 9.6 | – | – | 9.4 | 9.9 | 10.1 | 10.4 | 10.1 | 11.4 | 2012
Lower Junction City | 25.5 | – | – | – | – | – | 24.0 | – | – | 22.5 | 19.0 | 21.3 | 19.5 | 20.0 | 20.8 | 2014
Hocker Flat | 30.4 | 22.0 | 22.2 | 24.0 | 25.5 | 25.9 | 27.7 | – | 28.2 | 25.7 | 26.4 | 26.2 | 26.2 | 25.9 | 29.7 | 2005
Upper Conner Creek | – | – | – | – | – | – | – | – | – | – | – | – | – | 9.4 | 31.9 | 2025
Conner Creek | 17.5 | – | 17.3 | 14.8 | 15.8 | 16.6 | 19.0 | 18.0 | 17.8 | 16.8 | 17.8 | 17.5 | 17.5 | 17.1 | 18.0 | 2006
Wheel Gulch | 14.1 | – | – | 14.3 | 13.8 | 13.8 | 13.6 | – | – | 17.3 | 15.3 | 15.3 | 15.6 | 15.8 | 14.8 | 2011
Valdor Gulch | 28.4 | – | 28.4 | 24.0 | 27.9 | 28.2 | 29.9 | 29.4 | 29.4 | 28.2 | 30.4 | 30.4 | 30.6 | 28.7 | 24.7 | 2006
Elk Horn | 13.6 | – | – | 11.9 | 13.3 | 13.3 | 13.3 | 11.4 | – | 11.4 | 12.6 | 12.6 | 12.8 | 12.6 | 15.6 | 2006
Pear Tree Gulch | 7.2 | – | 7.4 | 6.7 | 6.7 | 6.9 | 6.7 | 6.7 | – | 6.7 | 6.9 | 6.9 | 6.4 | 6.4 | 7.9 | 2006
Hoopa Valley Tribe

## Slide 17: Summary of Changes by ESL
Hoopa Valley Tribe
35 channel rehabilitation sites (including 25 constructed and 10 planned sites)
  17 sites recovered
  4 Sites not recovered in 10 yrs
    4 sites
      Indian Creek
      Lower Junction City
      Hocker Flat
      Valdor Gulch
  4 Sites older than 10 yrs not recovered
    Dutch Creek(2020)
    Chapman Phase A (2019)
    Chapman Phase B (2021)
    Oregon Gulch (2023)
  Total Surplus/Deficit
    54.4 ac – 8.6 ac – 18.1 ac = +27.7 ac
-8.6 ac
+54.4 ac
-18.1 ac
2.0
2.0
6.4
7.7
1.0
3.2
0.7
3.7
Notes: +55.2 ac net increase

## Slide 18: Riparian Plantings
Riparian planting (treated as an open cover type in the analysis) –
As riparian plantings mature they are assigned a riparian cover type when they meet a given cover type’s assignment rules
Spatial distribution of riparian functional groups over time
Potential cover-based analyses:
  What are riparian plantings becoming (i.e, transition matrix)?
  What is the terrestrial value of that habitat?
Hoopa Valley Tribe
No Change

## Slide 19
2024 Mapping Study Objectives
Evaluate the success of core objectives:
  1) Riparian Area: Riparian vegetation will be more abundant following implementation of ROD management actions.
  2) Riparian plantings on existing and constructed floodplains will maintain or increase established vegetation.
  3) Diversity: Native riparian vegetation will be more diverse following implementation of ROD management actions.
Hoopa Valley Tribe

## Slide 20: Change to Riparian Hardwood Dominance
Cover type | Patch metric | 2003 | 2010 | 2014 | 2019 | Burned | 2024
Cottonwood | Area mapped (ac) | 50.48 | 42.80 | 58.37 | 58.51 | 0.89 | 57.40
 | Polygon Number | 178 | 228 | 509 | 438 | 3 | 722
 | Average size (ac) | 0.30 | 0.20 | 0.12 | 0.12 | 0.54 | 0.08
Narrowleaf–dusky willow | Area mapped (ac) | 205.42 | 192.05 | 313.38 | 298.55 | 9.49 | 268.51
 | Polygon Number | 640 | 863 | 1,504 | 1,300 | 24 | 1672
 | Average size (ac) | 0.32 | 0.22 | 0.22 | 0.25 | 0.99 | 0.09
White alder | Area mapped (ac) | 332.38 | 286.22 | 281.60 | 272.90 | 0.86 | 235.74
 | Polygon Number | 699 | 782 | 1,113 | 1,066 | 4 | 1815
 | Average size (ac) | 0.47 | 0.37 | 0.27 | 0.27 | 0.54 | 0.13
Oregon Ash | Area mapped (ac) | 8.77 | 21.15 | 46.25 | 44.16 | 0.53 | 74.04
 | Number | 44 | 41 | 567 | 485 | 2 | 1386
 | Average size (ac) | 0.20 | 0.52 | 0.08 | 0.09 | 0.26 | 0.05
Riparian Hardwood Cover Change (2014–2024)
Cottonwood ~ stable (58.4 → 57.4 ac)
  Recruitment ≈ mortality (limited expansion)
Narrowleaf–dusky willow ↓ (313.4 → 268.5 ac)
  Drivers: scour, channel rehab, fire (lower reaches)
  Polygons ↑ (1,504 → 1,672)
    Fragmentation of large stands → smaller patches
    Indicates reduced riparian encroachment
White alder ↓ (281.6 → 235.7 ac)
  Likely drivers: senescence, scour (restoration flows), channel rehab
  Average patch size ↓ (0.27 → 0.13 ac) with ↑ polygon count
Oregon ash ↑ (46.3 → 74.0 ac)
  Largest hardwood gain
  Suggests strong alignment with restoration flow recruitment
Note on interpretation
  Higher mapping resolution influences observed fragmentation trends
Hoopa Valley Tribe

## Slide 21: Change to Riparian Cover Diversity
Cover type richness (S)
Shannon diversity index (H’)
  Takes richness, relative abundance and evenness in account
  Higher value indicates higher
Maximum possible diversity (Hmax) is based on cover type richness
Pielou’s evenness index (J′)
  Ranges from 0 to 1,
    1 indicates that all cover types are represented equally
    0 indicates strong dominance by one or few cover types.
Hoopa Valley Tribe
Hmax = ln(S)
H′ = −Σ [pi ln (pi)]
J′ = H′ / Hmax

## Slide 22: Change to Riparian Cover Diversity
H′ declined in 2014 to 2019, then recovered in 2024.
Maximum possible diversity (Hmax) increased progressively across all three years, reflecting the expansion of available cover types.
Pielou’s evenness index (J′) demonstrated a consistent declining trend across the study period.
Metric | 2014 | 2019 | 2024
Riparian Cover type richness (S) | 24 | 24 | 37
Shannon diversity index (H′) | 2.13 | 2.00 | 2.23
Maximum Shannon diversity (Hmax) | 3.18 | 3.22 | 3.61
Pielou’s evenness index (J′) | 0.669 | 0.622 | 0.616
Hoopa Valley Tribe
Management recommendation:
-Track species-level diversity over time

## Slide 23: Objectives: Revisited
2024 Mapping Study Objectives
Evaluate the success of three core objectives:
  1) Riparian Area: Riparian vegetation will be more abundant following implementation of ROD management actions.
  2) Riparian plantings on existing and constructed floodplains will maintain or increase established vegetation.
  3) Diversity: Native riparian vegetation will be more diverse following implementation of ROD management actions.
Hoopa Valley Tribe
Total riparian: +50 ac since 2003
Last decade: +60 ac (2014-2024)

## Slide 24: Questions?
Hoopa Valley Tribe

## Slide 25: Native Riparian Cover
13
Hoopa Valley Tribe
Native riparian: −32 ac since 2003
Last decade: +28 ac (2014–2024)
Disturbance:
Scour
Development
CRS construction
Drought
Fire
Chart: Native Riparian Change
| 2003 | 2010 | 2014 | 2019 | 2024

Riparian | 931.8344 | 919.232 | 871.5199 | 853.502 | 899.548
Increased restoration flows
Drought (WY 2013–15) dry or critically dry
2014 methodological change