## Slide 1: Effects of gravel augmentation on juvenile salmonid rearing habitat
Prepared by Aaron Martin and Kyle DeJuilio, Yurok Tribal Fisheries

## Slide 2: Sawmill Main Channel
Pre-construction Mainstem habitat:
  1,150 m2 optimal
  6,572 m2 total
Three bars built during construction:
Low flow gravel augmentation
IC-2, IC-7, and IC-10 + meanders
Intent:
  Increase sinuosity
  Decrease radius of curvature
  Increase rearing habitat
Post-construction Mainstem habitat:
  1,844 m2 optimal
  7,052 m2 total
Revisit mainstem habitat
(post 2011 Rod Release):
  650 m2 optimal
  6,342 m2 total
What Happened?

## Slide 3: Sawmill Revist
Post-construction – Modest increases in rearing habitat
Revist – Habitat decreases to below pre-construction levels
IC-2 did not persist
IC-7 persists
  Major habitat contribution of the down steam alcove is now disconnected at base flow
  R-2 Channel meander persists
  This bar was amended and reinforced significantly during the summer of 2013

## Slide 4: Sawmill Revisit (IC-10)
Post-construction:
  Bar has diminished
  No habitat gains
Revisit:
  Bar is gone
  Modest habitat increase in area of R-8 channel meander
Result:
  No increase in sinuosity
  Depositional
  Net loss in mainstem habitat 3 years later

## Slide 5: Lower Reading Creek
Low flow gravel augmentation prescription:
  Alternating bars IC-7 and IC-8
  Intended to increase sinuosity
  Accompanied by R-5 and R-4 floodplain lowering and Channel meander
Intent:
  Increase sinuosity
  Decrease radius of curvature
  Increase rearing habitat

## Slide 6: Lower Reading Creek Habitat Results Pre-construction / Post-construction
Pre-construction:
Location of alternating bars to be constructed
Post-construction:
Alternating bars did not persist

## Slide 7: Trinity House Gulch
Two bars to be constructed:
IC-1
IC-3
  Accompanied by adjacent excavation of R-1 Channel meander
Intent:
  Increase sinuosity
  Decrease radius of curvature
  Increase rearing habitat

## Slide 8: Trinity House Gulch Pre-construction / Post Construction
Two Bars to be built:
IC-1
IC-3
Additional high flow augmentation bar upstream
Post-construction AND Post 2011 Rod Flow Release:
No constructed bars persist
Three new alluvial features have formed
Results:
  Good?
  Unintended

## Slide 9: Trinity House Gulch Naturally Formed bars
The habitat in the area has shifted from an abundance of cover associated habitat to habitat deemed suitable by depth and velocity
This would be expected from a newly formed alluvial feature

## Slide 10: Hoadley Gulch Construction
Bar constructed on inside of bend, floodplain lowered behind it for sc construction
Constructed bar has persisted
42% reduction in total habitat at constructed bar, switched from mostly optimal to predominately suitable (no cover)
2013
2009

## Slide 11: Lowden Meadows
Forced meander
  Point bar IC-2
  Forced meander R-3
Intent
  Increase channel sinuosity
  Decrease radius of curvature
  Increase rearing habitat

## Slide 12: Lowden Meadows – Forced Meander
Pre-construction main channel presmolt habitat:
  1,346 m2 optimal
  5,188 m2 total
Post-construction main channel + alcove presmolt habitat:
  1,703 m2 optimal
  8,337 m2 total
To be continued…..

## Slide 13: Different Results Similar Intent
Three times sediment used to build Lowden floodplain/bar
Wood jam built at top to protect bar
Persisted through 2011 high flow peak

## Slide 14: Cableway
Pre-construction main channel presmolt rearing habitat:
  1,586 m2 optimal
  6,031 m2 total
Four bars were constructed-oversized cobbles were used in some cases
Post-construction main channel
Presmolt rearing habitat:
  1,390 m2 optimal
  5,816 m2 total

## Slide 15: Cableway
Increasing habitat at higher flows
No berm, water spread out at higher flows
Bars eliminated small dip at ~500cfs
3 out of 4 bars persisted
Chart: Total Habitat
| 8.6366392500000266 | 11.128522050000001 | 19.283774849999876 | 34.263388500000012 | 57.200037000000002
Fry pre-construction | 2752.863 | 1829.3954 | 4205.232 | 5442.7274 | 9783.1367
Fry post-construction | 4767.4339 | 4848.5758 | 6454.8451 | 8849.7892 | 12095.2921
Presmolt pre-construction | 3743.5635 | 2433.0975 | 4972.3501 | 6037.2499 | 9961.6783
Presmolt post-construction | 6305.7595 | 6126.1628 | 7445.9288 | 9693.1652 | 12316.8332
Chart: DV, C
| 8.6366392500000266 | 11.128522050000001 | 19.283774849999876 | 34.263388500000012 | 57.200037000000002
Fry pre-construction | 1009.6551 | 453.7145 | 1548.7419 | 2880.5789 | 5602.3474
Fry post-construction | 1731.339 | 2288.2496 | 3369.3798 | 4181.2799 | 6083.6074
Presmolt pre-construction | 1261.3796 | 547.0147 | 1753.1872 | 3766.5882 | 6560.2588
Presmolt post-construction | 2029.3468 | 2618.9184 | 3963.6073 | 5382.4798 | 7554.9967

## Slide 16: Can we let the river do it?
  Is natural bar formation occurring at rehab sites?
  If so how is it affecting habitat?
  What are the conditions that are favorable to natural bar formation or persistence of constructed bars?

## Slide 17: Back to Lowden Meadows
There is a high flow gravel introduction site in the middle of the rehabilitation site.
  A naturally formed mid channel bar existed pre construction
  Feature R-4, a low bench, was designed to promote the growth and maintenance of this mid channel bar

## Slide 18: Promoting Natural Process
Changes to mid channel bar post-construction:
The mid-channel bar area (area above low flow wetted edge) increased from 236 m² to 558 m², a 136% increase
Winter base flow total habitat increased 1,048 m² or 69%
Chart: Total habitat
| 8.7000000000000011 | 11.4 | 20 | 34 | 53.9
Pre-construction | 1509.7598 | 1246.5558 | 793.0714 | 664.2729 | 780.0686
Post-construction | 2558.1575 | 2030.9465 | 1290.1296 | 792.8968 | 1424.5998

## Slide 19: Hocker Flat
Construction:
  Removal of riparian berm
  Floodplain lowering
Natural sediment source:
  The confluence of the Trinity with Canyon Creek is at the upstream end of the site

## Slide 20: Natural Mid Channel Bar Formation

## Slide 21: Upper Dark Gulch Project Design
Project Goal- Increase salmonid rearing habitat at all flows
Design Elements include:
Berm Removal
Floodplain lowering
Side channel creation
Addition of large wood and riparian plantings
24,000 CY excavation
NO BAR CONSTRUCTION!

## Slide 22: Upper Dark Gulch Pre vs Post-construction
Chart: Optimal Habitat
| 300 | 450 | 700 | 1200 | 2000
Post | 633.8687 | 534.2955 | 381.7238 | 262.2828 | 261.0521
Pre | 418.4686 | 256.3406 | 240.6315 | 547.3772
Chart: Total Habitat
| 300 | 450 | 700 | 1200 | 2000
Post | 2806.4763 | 2515.5236 | 2148.5193 | 1855.0075 | 2169.3179
Pre | 1986.078 | 1165.9859 | 872.4529 | 1354.8583

## Slide 24: 2011 High Flow

## Slide 25: Upper Dark Gulch Revisit (post high flow)
Chart: Optimal habitat
| 300 | 450 | 700 | 1200 | 2000
Post | 633.8687 | 534.2955 | 381.7238 | 262.2828 | 261.0521
Pre | 418.4686 | 256.3406 | 240.6315 | 547.3772
Revisit | 694.5896 | 897.0636 | 1363.8622 | 3117.6701 | 5576.1658
Chart: Total habitat
| 300 | 450 | 700 | 1200 | 2000
Post | 2806.4763 | 2515.5236 | 2148.5193 | 1855.0075 | 2169.3179
Pre | 1986.078 | 1165.9859 | 872.4529 | 1354.8583
Revisit | 2822.4928 | 2994.5201 | 3346.6118 | 7633.2633 | 13299.9339

## Slide 26: What Happened?!?

## Slide 27: Topographic difference
Subtracted 2009 surface from 2013 surface
Huge area of deposition
Over 7 ft of deposition is some locations
~7600 yds³

## Slide 28: Cross section profile
Chart: Station

## Slide 29
Process!!

## Slide 30: Riparian Development
2009
2013

## Slide 31: Observations
Most low flow bar placements did not persist. Especially where significant floodplain lowering did not occur
Low flow bar placements that did persist used more material and LWD for protection, or a combination of larger substrate, lowering of floodplains and placement on inside of bend
Placed bars must create and sustain backwaters or alcoves to maintain or increase low flow habitat
Combination of filling in main channel and floodplain lowering can create large increases in habitat at higher flows