## Slide 1: Straw Dog for Information and Analyses to Support Gravel Augmentation Master Plan
For July 30, 2014 Gravel Augmentation Workgroup Meeting

## Slide 2: Goal Statement:
Goal: outcome statements that define accomplishment
Goal:
“Identify and prioritize locations where placement of coarse gravel will improve habitat on a reach scale”

## Slide 3
FLOW REGIME
SEDIMENT
WOOD
TRIBUTARY INPUTS (SEDIMENT)
BANK EROSION
WOOD
DEPOSITION
SEDIMENT
WOOD
CONDITION:
SEDIMENT MOBILITY
HABITAT QUALITY
STRUCTURAL CONTROL
Will management actions (gravel augmentation, flow adjustment, channel rehabilitation) increase habitat?

## Slide 4: Information Needs
Identify Sediment Sources and Sinks at Reach Scale
Identify Sediment Mobility and Bank Erosion Potential
Channel Management Map

## Slide 5: Identify Sediment Sources and Sinks
Work in Progress
  Geologic Supply (Smelser; Gaeuman)
  Tributary Supplies (Gaeuman)
  Sediment Competence and Transport (Gaeuman)
Work to be Done:
  Reach Based Sediment Budget
  1-D Sediment Transport Modeling (Existing and Management Actions)
  Quantify Linkages between Reaches
  Quantify Legacy Sediment

## Slide 6: Identify Sediment Mobility and Bank Erosion Potential
Work in Progress
  2-D Model
  Substrate Mapping (HVT/USFWS/TRRP)
  Initial Bank Strength Evaluation (Gaueman)
Work needs:
  Select and Implement Bank Strength Assessment Protocol
  Identify Sediment Mobility/Armoring at Reach Scale
  Identify Current and Potential Reach Form (Alluvial/Semi/Non)

## Slide 7: Channel Management Map
Map Managed Alluvial Channel Corridor Limits
    Geologic Controls
    Historical Migration Limits and Patterns
    Infrastructure
    Management Constraints
    Reach Form
    Substrate and Sediment Transport Properties
    Habitat Quality/Quantity (2-D Model)
Provides Information to Support Analysis of:
    Migration Potential
    Planform Development Potential
    Management Decisions

## Slide 8: Work Plan
Prepare Additional Analyses
  Hydraulic and Morphodynamic Models
  Substrate Map
  Reach Scale Sediment Budget Analysis
  Bed and Bank Stability Assessment
  Geologic and Form Controls
  Channel Evolution Model
Analysis Phase
  Evaluate alternate management action scenarios (flow releases, gravel augmentation, and channel rehabilitation) in terms of increasing quality and quantity of habitat within individual reaches.