## Slide 1: Bucktail Channel Rehabilitation
Version 3.0
Dr. Mike Dixon, Implementation Branch Chief

## Slide 4: Highlights

## Slide 5
IC-2 Side Channel

## Slide 6
Beaver dam analog
Notes: Functioning as designed. Up to 5 feet deep in spots but holds large areas of shallow water. Began with a small seasonal wetland, so there is already some established vegetation.

## Slide 7
Riparian salvage planting
Notes: Trying to salvage removed riparian vegetation by cutting, excavating, keeping them wet, digging to groundwater, and immediately planting.

## Slide 8
Significant field design changes

## Slide 9: Vehicle barriers
Notes: No plan was put in place in advance to keep vehicles from driving out onto extensive revegetated upland areas. Logs are being put in place now.
No safety barrier to prevent vehicles from driving over the edge into R6 were specified; rocks are being put in place.
Also, paving of the new road was not specified in the PWS due to an oversight. Details of modification to allow this work to proceed are being worked out; anticipate paving in 30 days using unexpended construction funds with Yurok Tribe.

## Slide 10: R-5, R-6 floodplain lowering
Notes: R5 originally a large flat 4500 cfs floodplain, changed to include 300-4500 surfaces including extensive 2000 cfs benches. Has live groundwater contribution and will contain both emergent wetland and riparian veg
R6 was initially constructed with linear sides and too close to the road edge; modified to be more complex and safer for vehicles on access road

## Slide 11: IC-1 point bar changed to transverse riffle

## Slide 12
ELJ-1 and 2; Mainstem channel relocation/split flow became low flow side channel
Notes: Lessons learned – identify potential design issues before construction, clarify who has decision responsibility for field design changes
Out of basin designers are not ideal.
Need to balance large wood design complexity with constructability and liability

## Slide 13: Landowner issues
Outreach
  Public meeting
  Direct mailing
  Landowner meeting
Lessons learned
  Impacts of noise may be pronounced
  Need to do proactive targeted outreach to recreational entities and vacation rentals
  A little goodwill goes a long way with some

## Slide 14: Questions?