## Slide 1
2018 Hydrologic Update
Projections for 2019 Water Year
September 5, 2018

## Slide 2
WY18: Upper Klamath Basin Precipitation
Notes: 2
It’s been a dry year, with snow water equivalent peaking at 59% of the historical average in March. Currently, the Basin is 78% of the average water year-to-date precipitation. Drier conditions have persisted in the lower elevations southern portions of Klamath County.

## Slide 3
Notes: The lack of precipitation has resulted in cumulative inflows, since October 1, 2017, consistently between the 80 and 90 percent exceedance curves.

## Slide 4: 2018 Water Operations Constraints
2017 Court Injunction
1. Surface Flushing Flow: 6,030 cfs for 72 hours (November 1 – April 30)
2. Deep Flushing Flow: 11,250 cfs for 24 hours from February 15 - May 31 (Not required in 2018)
3. Emergency Dilution Flow: Up to 50,000 AF, if disease conditions are observed from April 1 - June 15, or 80% juvenile salmon outmigration, whichever occurs first
**Injunctive flows are additive to 2013 Biological Opinion required flows and lake levels
Notes: In addition to the dry hydrologic conditions, there were also additional constraints placed on this water from a Court injunction that was imposed in 2017.
In 2016, the Yurok and Hoopa Valley Tribes and environmental groups filed Federal lawsuits alleging violation of the ESA, seeking injunctive relief. In March 2017, the Federal District Court for Northern California issued an Injunction requiring Reclamation to implement three kinds of augmented flows to the Klamath River to combat fish disease in endangered Coho salmon, until a reinitiation of formal consultation on Klamath Project operations is complete.
The three types of required flows under the injunction are: Surface Flushing, Deep Flushing, Emergency flows. Deep Flushing Flows (are required every other year and were implemented in 2017 thus are not required in 2018).
The Injunction is clear that in all other respects the 2013 Biological Opinion on Klamath Project operations and incidental take statement remain in effect pending completion of the reinitiated formal consultation --currently scheduled for February 2020.
Additionally, the Court stated that:
  A) in no event shall the prescribed flows interfere with the conditions necessary to protect endangered suckers and
  B) Reclamation will manage the Klamath Project in a manner that will not will not:
    1) preclude the ability to provide Reserve Water to implement up to 50 TAF of emergency dilution flows and/or
    2) interfere with its ability to meet its obligations under the ESA with regard to endangered suckers and/or their critical habitat.

## Slide 5
Notes: The surface flushing flow occurred in early April, which coincided with a storm event. Still, the flow required approximately 40 TAF from stored water in UKL.
The emergency dilution flows were triggered in early May and required 50 TAF of water from UKL for disease mitigation.
Both the emergency dilution flows and surface flushing flows were ultimately removed from potential project supply.

## Slide 6
Notes: Despite both of those required flows, we have exceeded all of the end of month thresholds in UKL and are projected to exceed the absolute minimum elevation of 4,137.72 feet by approximately 0.75 feet.

## Slide 7
Project Deliveries
Available Project Supply = 234 TAF (60% of full supply of 390 TAF)
Notes: Project supply of 234 TAF in 2018. Given the recent uptick in demand in August, the project only has 33 TAF for the remainder of 2018 (67% of the historic average demand of 48.5 TAF).
Again, the project supply was impacted by implementation of the flushing and emergency dilution.

## Slide 8
September – November
Forecast
Notes: 8
Ocean conditions are shaping up for El-Nino conditions: over the next three months, September – November the National Weather Service is projecting above average temperatures and below average precipitation.

## Slide 9
2019 Outlook
Potential Sideboards:
2017 Injunction
  Surface and deep flushing flow
  Potentially emergency dilution flows (if triggers are eclipsed)
  Klamath Tribes Litigation
  If Preliminary Injunction is pursued and successful, Reclamation would be required to maintain higher UKL elevations
Notes: Similar sideboards for the 2019 Water year:
1) We will have to implement a surface flushing flow of 6,030 cfs and a deep flushing flow of 11,250 cfs. We will attempt to implement both flows in one event (as was the case in 2017), but the deep flushing flow will be highly dependent on large accretion events.
2) Reclamation will convene a meeting with the litigants to try to identify flexibility and potential modifications for the emergency dilution flow triggers. That said, Reclamation will likely be required to operate the Project in a manner that doesn’t preclude our ability to make 50 TAF available for a dilution flow.
3) The Klamath Tribes hearing is scheduled for early March, with a decision from the Oregon Court no later than April 1, 2019. If the Klamath Tribes persue a preliminary injunction, and is successful, it would require Reclamation to hold UKL elevations higher, to their adjudicated claims. If successful, this would have a devastating impact to Project operations and our ability to meet required flows for BiOp and 2017 injunction implementation.